INTERNATIONAL ORGANIZATION FOR STANDARDIZATION

ORGANISATION INTERNATIONALE DE NORMALISATION

ISO/IEC JTC1/SC29/WG11

CODING OF MOVING PICTURES AND ASSOCIATED AUDIO

ISO/IEC JTC1/SC29/WG11N0701

MPEG94/

March 1994

Source		: Systems Subgroup

Title		: ISO/IEC 13818-1 (MPEG-2 Systems)

Purpose		: Review

Status		: Interim edited CD

The following is an interim version of the systems specification for the purpose of documenting the agreements reach at the March 1994 Paris meeting and the editing changes submitted by national body members and approved by the systems subgroup.

Some significant technical matters were resolved but are not fully documented in this document. Examples include:

T-STD  -  leaky bucket model

PES STD to constrain PES overhead

Splicing support

PCR tolerance

Remultiplexing support

TITLE PAGE PROVIDED BY ISO

© ISO/IEC 1993

All rights reserved.  No part of this publication may be reproduced or utilized in any form or by any means, electronic or mechanical, including photocopying and microfilm, without permission in writing from the publisher.

ISO/IEC Copyright Office • Case Postale 56 • CH1211 Genève 20 • Switzerland

Printed in Switzerland.

2128 Thu 24 Mar 1994

| CONTENTS | Page |  |  |  |
| --- | --- | --- | --- | --- |

CONTENTS	ii

List of Figures	iv

List of Syntax Tables	v

List of Equations	vii

FOREWORD	viii

INTRODUCTION - PART 1 SYSTEMS	ix

0.1 Transport Stream	xi

0.2 Program Stream	xiii

0.3 Conversion between Transport Stream and Program Stream	xiii

0.5 Timing model	xiv

0.6 Conditional access	xv

0.7 Multiplex-wide Operations	xv

0.8 Individual stream operations	xv

0.8 1 De-multiplexing	xv

0.8 2 Synchronization	xvi

0.8 3 Relation to compression layer	xvi

0.9 System reference decoder	xvi

0.10 Applications	xvii

Section 1: General	1

1.1 Scope	1

1.2 References	1

2 TECHNICAL ELEMENTS	3

2.1 Definitions	3

2.2 Symbols and abbreviations	5

2.2.1Arithmetic operators	5

2.2.2 Logical operators	6

2.2.3 Relational operators	6

2.2.4 Bitwise operators	7

2.2.5 Assignment	7

2.2.6 Mnemonics	7

2.2.7 Constants	8

2.3 Method of describing bit stream syntax	8

2.4 Bitstream requirements	9

2.4.1 Transport Stream coding structure and parameters	9

2.4.2 Transport Stream system target decoder	11

2.4.3 Specification of the system Transport Stream syntax	16

2.4.4 Program Stream coding structure and parameters	29

2.4.5 Program Stream system target decoder	30

2.4.6 Specification of the Program Stream syntax	33

2.4.7 Program specific information	43

2.4.8 Program and elementary stream descriptors	52

2.4.9 Restrictions on the multiplexed stream semantics	60

2.4.10 Constrained system parameter stream	63

2.4.11 Compatibility with ISO/IEC 11172	65

Annexes

A	Digital Storage Medium Command and Control [DSM CC]	66

B	ISO/IEC 13818 Systems Timing Model and Application Implications	77

C	Program Specific Information	87

D	Service Information Descriptors	94

E	Data Transmission Applications	96

F	Graphics of Syntax for ISO/IEC 13818	97

G	General Information	102

H	List of companies having provided patent statements for ISO/IEC 13818	103

List of Figures

0-1 -- Simplified overview of ISO/IEC 13818 scope	x

0-2 -- Prototypical transport demultiplexing and decoding example	xii

0-3 -- Prototypical transport multiplexing example	xii

0-4 -- Prototypical transport to program stream conversion	xii

0-5 -- Prototypical program stream decoder	xiii

2-6 -- ISO/IEC 13818 Transport Stream system target decoder notation	11

2-7 -- ISO/IEC 13818 Program Stream system target decoder notation	30

A-1 -- Configuration of DSM CC application	68

A-2 -- DSM CC bitstream decoded as a standalone bitstream	69

A-3 -- DSM CC bitstream decoded as part of the system bitstream	69

B-1 -- Constant delay model	77

B-2 -- STC recovery using PLL	81

C-1 -- Program and network mapping relationships	89

F-1 -- Transport Stream syntax diagram	97

F-2 -- PES packet syntax diagram	98

F-3 -- Conditional access section diagram	98

F-4 -- TS program map section diagram	99

F-5 -- Private section diagram	100

F-6 -- Program Stream diagram	101

F-7 -- Program Stream map diagram	101

List of Syntax Tables

2-1 -- Next start code

2-2 -- ISO/IEC 13818 Transport Stream

2-3 -- ISO/IEC 13818 transport header

2-4 -- Scrambling control values

2-5 -- Adaptation field control values

2-6 -- Transport Stream adaptation header

2-7 -- PES Packet

2-8 -- PES scrambling control values

2-9 -- Trick mode control values

2-10 -- Coefficient selection values

2-11 -- Freeze frame control values

2-12 -- Fast reverse control values

2-13 -- Program specific information

2-15 -- Program association section

2-16 -- table_id assignment values

2-17 -- Conditional access section

2-18 -- Transport Stream program map section

2-19 -- Private section

2-20 -- ISO/IEC 13818 Program Stream

2-21 -- ISO/IEC 13818 Program Stream pack

2-22 -- Program Stream pack header

2-23 -- Program Stream system header

2-24 -- Stream_id table

2-25 -- Program Stream map

2-26 -- Stream type assignments

2-27 -- PES packet header for Program Stream directory

2-28 -- PES packet payload for Program Stream directory

2-29 -- Intra_coded indicator

2-30 -- Coding_parameters indicator

2-31 -- Stream descriptors

2-32 -- Video stream descriptor

2-33 -- Video coding version

2-34 -- Audio stream descriptor

2-35 -- Audio coding version

2-36 -- Hierarchy descriptor

2-37 -- Hierarchy descriptor values

2-38 -- Registration descriptor

2-39 -- Registration authority committee

2-40 -- Data stream alignment descriptor

2-41 -- Video stream alignment values

2-42 -- Audio stream alignment values

2-43 -- Target background grid descriptor

2-44 -- Video window descriptor

2-45 -- Conditional access descriptor

2-46 -- ISO 639 language descriptor

2-47 -- System clock descriptor

2-48 -- Multiplex buffer utilization descriptor

A-1 -- ISO/IEC 13818 DSM CC

A-2 -- Command_id assigned values

A-3 -- DSM_CC control

A-4 -- Select mode assigned values

A-5 -- DSM CC Acknowledgement

A-6 -- Time code

A-1 -- Program association table bandwidth usage (bps)

A-2 -- Program table bandwidth usage (bps)

A-1 -- Program descriptor example

A-2 -- Program sub-descriptor

A-1 -- PES packet header example

A-1 -- List of companies supplying patent statements

List of Equations

2-1 -- PCR base equation

2-2 -- PCR extension equation

2-3 -- Program Clock Reference equation

2-4 -- Calculation of input arrival time

2-5 -- Transport rate calculation

2-6 -- Latency calculation

2-7 -- System information main buffer transfer rate

2-8 -- Calculation of presentation timestamp

2-9 -- Calculation of decode timestamp

2-10 -- Calculation of elementary stream clock reference

2-11 -- Calculation of elementary stream clock reference extension

2-12 -- Calculation of elementary stream clock reference

2-13 -- Buffer size for audio stream

2-14 -- Buffer size for video stream

2-15 -- System clock reference base calulation

2-16 -- System clock reference extension

2-17 -- System clock reference calculation

2-18 -- Arrival time calculation

2-19 -- System clock reference base calculation

2-20 -- System clock reference extension calculation

2-21 -- System clock reference calculation

2-22 -- System clock reference interval calculation

2-23 -- Ratio of system clock frequency and audio sample rate

2-24 -- Ratio of system clock frequency to video picture rate

2-25 -- Clock accuracy determination

2-26 -- Multiplex buffer utilization calculation

2-27 -- Packet rate calculation

2-28 -- Maximum packet rate calculation

2-29 -- Sample rate locking in Transport Stream

2-30 -- Ratio of system clock frequency to video picture rate

FOREWORD

FOREWORD PROVIDED BY ISO

INTRODUCTION

The systems part of this Recommendation | International Standard addresses the combining of one or more elementary streams of video and audio, as well as other data, into single or multiple streams which are suitable for storage or transmission. Systems coding follows the syntactical and semantic rules imposed by this specification and provides information to enable synchronized decoding of decoder buffers over a wide range of retrieval or receipt conditions.

System coding shall be specified in two forms: the Transport Stream and the Program Stream. Each is optimized for a different set of applications. Both the Transport Stream and Program Stream defined in this Recommendation | International Standard provide coding syntax which is necessary and sufficient to synchronize the decoding and presentation of the video and audio information, while ensuring that data buffers in the decoders do not overflow or underflow. Information is coded in the syntax using time stamps concerning the decoding and presentation of coded audio and visual data and time stamps concerning the delivery of the data stream itself. Both stream definitions are packet-oriented multiplexes.

The basic multiplexing approach for single video and audio elementary streams is illustrated in figure 0-1 on page x . The video and audio data is encoded as described in Parts 2 and 3 of this Recommendation | International Standard. The resulting compressed elementary streams are packetized to produce PES packets. Information needed to use PES packets independent of either Transport Streams or Program Streams may be added when PES packets are formed. This information is not needed and need not be added when PES packets are further combined with system level information to form Transport Streams or a Program Streams. This systems standard covers those processes to the right of the vertical dashed line.

Figure 0-1 -- Simplified overview of ISO/IEC 13818 scope0-1

The Program Stream is analogous and similar to ISO/IEC 11172 Systems Multiplex. It results from combining one or more streams of PES packets, which have a common time base, into a single stream. The Program Stream definition can also be used to encode multiple audio and video elementary streams into multiple Program Streams, all of which have a common time base.

Like the single Program Stream, all elementary streams can be decoded with synchronization.

The Program Stream is designed for use in relatively error-free environments and is suitable for applications which may involve software processing of system information such as interactive multi-media applications. Program Stream packets may be of variable and relatively great length.

The Transport Stream combines one or more programs with one or more independent time bases into a single stream. PES packets made up of elementary streams that form a program share a common timebase. The Transport Stream is designed for use in environments where errors are likely, such as storage or transmission in lossy or noisy media. Transport Stream packets are 188 bytes in length.

Program and Transport Streams are designed for different applications and their definitions do not strictly follow a layered model. It is possible and reasonable to convert from one to the other, however, one is not a subset or superset of the other. In particular, extracting the contents of a program from a Transport Stream and creating a valid Program Stream is possible and is accomplished through the common interchange format of PES packets, but not all of the fields needed in a Program Stream are contained within the Transport Stream; some must be derived. The Transport Stream may be used to span a range of layers in a layered model, and is designed for efficiency and ease of implementation in high bandwidth applications.

The scope of syntactical and semantic rules set forth in the systems specification differ: the syntactical rules apply to systems layer coding only, and do not extend to the compression layer coding of the video and audio specifications;  by contrast, the semantic rules apply to the combined stream in its entirety.

The systems specification does not specify the architecture or implementation of encoders or decoders, nor those of multiplexors or demultiplexors. However, bit stream properties do impose functional and performance requirements on encoders, decoders, multiplexors and demultiplexors. For instance, encoders must meet minimum clock tolerance requirements. Notwithstanding this and other requirements, a considerable degree of freedom exists in the design and implementation of encoders, decoders, multiplexors and demultiplexors.

0.1	Transport Stream

0.1

The Transport Stream is a stream definition which is tailored for communicating or storing one or more programs of ISO/IEC 13818 coded data and other data in environments in which significant errors may occur. Such errors may be manifested as bit value errors or loss of packets.

The ISO/IEC 13818 Transport Stream may be constructed by any method that results in a valid stream. It is possible to construct Transport Streams containing one or more programs from elementary coded data streams, from Program Streams, or from other Transport Streams which may themselves contain one or more programs.

The Transport Stream is designed in such a way that several operations on a Transport Stream are possible with minimum effort. Among these are:

1. Retrieve the coded data from one program within the Transport Stream, decode it and present the decoded results as shown in figure 0-2 on page xii .

2. Extract the Transport Stream packettransport packets from one program within the Transport Stream and produce as output a different Transport Stream with only that one program as shown in figure 0-3 on page xii .

3. Extract the Transport Stream packettransport packets of one or more programs from one or more Transport Streams and produce as output a different Transport Stream (not illustrated).

4. Extract the contents of one program from the Transport Stream and produce as output a Program Stream containing that one program as shown in figure 0-4 on page xii .

5. Take a Program Stream, convert it into a Transport Stream to carry it over a lossy environment, and then recover a valid, and in certain cases, identical Program Stream.

Figure 0-2 on page xii  and figure 0-3 on page xii  illustrate prototypical demultiplexing and decoding systems which takes as input an ISO/IEC 13818 Transport Stream. Figure 0-2 on page xii  illustrates the first case, where a Transport Stream is directly demultiplexed and decoded. ISO/IEC 13818 Transport Streams are constructed in two layers: a system layer and a compression layer. The input stream to the Transport Stream decoder has a system layer wrapped about a compression layer. Input streams to the Video and Audio decoders have only the compression layer.

Operations performed by the Transport Stream decoder either apply to the entire ISO/IEC 13818 Transport Stream ("multiplex-wide operations"), or to individual elementary streams ("stream-specific operations").  The ISO/IEC 13818 transport system layer is divided into two sub-layers, one for multiplex-wide operations (the transport packet layer), and one for stream-specific operations (the PES packet layer).

A prototypical audio/video Transport Stream decoder is also depicted in figure 0-2 on page xii  to illustrate the function of a decoder. The architecture is not unique -- some Transport Stream system decoder functions, such as decoder timing control, might equally well be distributed among elementary stream decoders and the Data Link Specific Decoder -- but this figure is useful for discussion. Likewise, indication of errors detected by the data link specific decoder to the individual audio and video decoders may be performed in various ways and such communications paths are not shown in the diagram. The prototypical decoder design does not imply any normative requirement for the design of an ISO/IEC 13818 Transport Stream decoder. Indeed non-audio/video data is also allowed, but not shown.

Figure 0-2 -- Prototypical transport demultiplexing and decoding example0-2

Figure 0-3  illustrates the second case, where a Transport Stream containing multiple programs is converted into a Transport Stream containing a single program: In the case shown in figure 0-3  the remultiplexing operation will include the correction of Program Clock Reference (PCR) timestamps to account for the change in arrival of timestamps.

Figure 0-3 -- Prototypical transport multiplexing example0-3

Figure 0-4  below illustrates a case in which an ISO/IEC 13818 multi-program Transport Stream is first demultiplexed then converted into an ISO/IEC 13818 Program Stream.

Figure 0-4 -- Prototypical transport to program stream conversion0-4

Figure 0-3 on page xii  and figure 0-4 on page xii  indicate that it is possible and reasonable to convert between different types and configurations of ISO/IEC 13818 Transport Streams. There are specific fields defined in the Transport Stream and Program Stream syntaxes which facilitate the conversions illustrated. There is no requirement that specific implementations of demultiplexors or decoders include all of these functions.

0.2	Program Stream

0.2

As in the case of Transport Stream, a prototypical audio/video Program Stream decoder system is depicted in figure 0-5  to illustrate the function of a decoder.  The architecture is not unique -- System Decoder functions including decoder timing control might equally well be distributed among elementary stream decoders and the Medium Specific Decoder -- but this figure is useful for discussion.  The prototypical decoder design does not imply any normative requirement for the design of an ISO/IEC 13818 Program Stream decoder.  Indeed non-audio/video data is also allowed, but not shown.

Figure 0-5 -- Prototypical program stream decoder0-5

The prototypical ISO/IEC 13818 Program Stream decoder shown in figure 0-5  is composed of System, Video, and Audio decoders conforming to Parts 1, 2, and 3, respectively, of this Recommendation | International Standard.   In this decoder the multiplexed coded representation of one or more audio and/or video streams is assumed to be stored on a digital storage medium (DSM), or network, in some medium-specific format.  The medium specific format is not governed by this Recommendation | International Standard, nor is the medium-specific decoding part of the prototypical ISO/IEC 13818 Program Stream decoder.

The prototypical decoder accepts as input an ISO/IEC 13818 Program Stream and relies on a Program Stream Decoder to extract timing information from the stream.  The Program Stream Decoder demultiplexes the stream, and the elementary streams so produced serve as inputs to Video and Audio decoders, whose outputs are decoded video and audio signals.  Included in the design, but not shown in the figure, is the flow of timing information among the Program Stream Decoder, the Video and Audio Decoders, and the Medium Specific Decoder. The Video and Audio Decoders are synchronized with each other and with the DSM using this timing information.

ISO/IEC 13818 Program Streams are constructed in two layers: a system layer and a compression layer.  The input stream to the Program Stream Decoder has a system layer wrapped about a compression layer.  Input streams to the Video and Audio decoders have only the compression layer.

Operations performed by the Program Stream Decoder either apply to the entire ISO/IEC 13818 Program Stream ("multiplex-wide operations"), or to individual elementary streams ("stream-specific operations").  The ISO/IEC 13818 Program system layer is divided into two sub-layers, one for multiplex-wide operations (the pack layer), and one for stream-specific operations (the PES packet layer).

0.3	Conversion between Transport Stream and Program Stream

0.3

It is possible and reasonable to convert between Transport Streams  and Program Streams by means of PES packets. This results from the specification of Transport Stream and Program Stream as embodied in clause 2.4.1 on page 9  and clause 2.5.1 on page 40  of the normative requirements of this Recommendation | International Standard. PES packets may, with some constraints, be mapped directly from the payload of one multiplexed bit stream into the payload of another multiplexed bit stream. It is possible to identify the correct order of PES packets in a program to assist with this.

Certain other information necessary for conversion, e.g. the relationship between elementary streams, is available in tables and headers in both streams. Such data must be available and correct in any stream before and after conversion.

Not all Transport Streams will have been formed from Program Streams but it is possible to create a valid Program Stream from a valid Transport Stream.

0.4	Packetized Elementary Stream

0.4

Transport Streams and Program Streams are each logically constructed from PES packets, as indicated in the syntax definitions in clause 2.4.3.6 on page 21. PES packets shall be used to convert between Transport Streams and Program Streams; in some cases the PES packets need not be modified when performing such conversions. PES packets may be much larger than the size of a Transport Stream packettransport packet.

A continuous sequence of PES packets of one elementary stream with one stream ID may be used to construct a PES Stream. When PES packets are used to form a PES stream, they shall include Elementary Stream Clock Reference (ESCR) fields and Elementary Stream Rate (ES_Rate) fields, with constraints as defined in clause 2.4.3.7 on page 24. The PES stream data shall be contiguous bytes from the elementary stream in their original order. PES streams do not contain some necessary system information which is contained in Program Streams and Transport Streams. Examples include the information in the Pack Header, System Header, Program Stream Map, Program Stream Directory, Program Map Table, and elements of the Transport Stream packettransport packet syntax.

The PES Stream is a logical construct that may be useful within implementations of this standard; however it is not defined as a stream for interchange and interoperability. Applications requiring streams containing only one elementary stream can use Program Streams or Transport Streams which each contain only one elementary stream. These streams contain all of the necessary system information. Multiple Program Streams or Transport Streams, each containing a single elementary stream, can be constructed with a common time base and therefore carry a complete program, i.e. with audio and video.

0.5	Timing model

0.5

ISO/IEC 13818 Systems, Video and Audio all have a timing model in which the end-to-end delay from the signal input to an encoder to the signal output from a decoder is a constant. This delay is the sum of encoding, encoder buffering, multiplexing, communication or storage, demultiplexing, decoder buffering, decoding, and presentation. As part of this timing model all video pictures and audio samples are presented exactly once, unless specifically coded to the contrary, and the inter-picture interval and audio sample rate are the same at the decoder as at the encoder. The system stream coding contains timing information which can be used to implement systems which embody constant end-to-end delay. It is possible to implement decoders which do not follow this model exactly; however in such cases it is the decoder's responsibility to perform in an acceptable manner. The timing is embodied in the normative specifications of this standard, which must be adhered to by all valid bit streams, regardless of the means of creating them.

All timing is defined in terms of a common system clock, referred to as a System Time Clock. In the Program Stream this clock may have an exactly specified ratio to the video or audio sample clocks, or it may have an operating frequency which differs slightly from the exact ratio while still providing precise end to end timing and clock recovery.

In the Transport Stream the system clock frequency is constrained to have the exactly specified ratio to the audio and video sample clocks at all times; the effect of this constraint is to simplify sample rate recovery in decoders.

0.6	Conditional access

0.6

Encryption and scrambling for conditional access to programs encoded in the Program and Transport Streams is supported by the system data stream definitions. Conditional access mechanisms are not specified here. The stream definitions are designed so that implementation of practical conditional access systems is reasonable, and there are some syntactical elements specified which provide specific support for such systems.

0.7	Multiplex-wide operations

0.7

Multiplex-wide operations include the coordination of data retrieval off the DSM or data link, the adjustment of clocks, and the management of buffers.  The tasks are intimately related.  If the rate of data delivery off the data link or DSM is controllable, then data delivery may be adjusted so that decoder buffers neither overflow nor underflow;  but if the data rate is not controllable, then elementary stream decoders must slave their timing to the data source to avoid overflow or underflow.

Program Streams are composed of packs whose headers facilitate the above tasks.  Pack headers specify intended times at which each byte is to enter the Program Stream Decoder from the data source, and this target arrival schedule serves as a reference for clock correction and buffer management.  The schedule need not be followed exactly by decoders, but they must compensate for deviations about it.

Similarly, Transport Streams are composed of Transport Stream packettransport packets with headers containing information which specifies the times at which each byte is intended to enter a Transport Stream Decoder from the data source. This schedule provides exactly the same function as that which is specified in the Program Stream.

An additional multiplex-wide operation is a decoder's ability to establish what resources are required to decode a Transport Stream or Program Stream.  The first pack of each Program Stream conveys parameters to assist decoders in this task.  Included, for example, are the stream's maximum data rate and the highest number of simultaneous video channels. The Transport Stream likewise contains globally useful information.

The Transport  Stream and Program Stream each contain information which identifies the pertinent characteristics of and relationships between the elementary streams which constitute each program. Such information may include the language spoken in audio channels, as well as the relationship between video streams when multi-layer video coding is implemented.

0.8	Individual stream operations (PES Packet Layer)

0.8

The principal stream-specific operations are 1) de-multiplexing, and 2) synchronizing playback of multiple elementary streams.  These topics are discussed next.

0.8.1	De-multiplexing

0.8.1

On encoding, Program Streams are formed by multiplexing elementary streams, and Transport Streams are formed by multiplexing elementary streams, Program Streams, or the contents of other Transport Streams.  Elementary streams may include private, reserved, and padding streams in addition to ISO/IEC 13818 audio and video streams. The streams are temporally subdivided into packets, and the packets are serialized.  A PES packet contains coded bytes from one and only one elementary stream.

In the Program Stream both fixed and variable packet lengths are allowed subject to constraints as specified in clause 2.5.1 on page 40 and clause 2.5.2 on page 41 of ISO/IEC 13818-1. For Transport Streams the packet length is 188 bytes. Both fixed and variable PES packet length are allowed, but will be relatively long in most applications.

On decoding, de-multiplexing is required to reconstitute elementary streams from the multiplexed Program Stream or Transport Stream. Stream_id codes in Program Stream packet headers, and Packet ID codes in the Transport Stream make this possible.

0.8.2	Synchronization

0.8.2

Synchronization among multiple elementary streams is effected with presentation time stamps (PTS) in the Program and Transport bit streams.  Time stamps are generally in units of 90kHz, but the System Clock Reference (SCR), the Program Clock Reference (PCR) and the optional Elementary Stream Clock Reference (ESCR)  have extensions with a resolution of 27MHz.  Decoding of N elementary streams is synchronized by adjusting the decoding of streams to a common master time base rather than by adjusting the decoding of one stream to match that of another.  The master time base may be one of the N decoders' clocks, the DSM or channel clock, or it may be some external clock.

Each program in a Transport Stream, which contains multiple programs,  has its own time base. The time bases of different programs within such a stream may be different.

Because presentation time-stamps (PTS) apply to the decoding of individual elementary streams, they reside in the PES packet layer of both the Transport Streams and Program Streams. End-to-end synchronization occurs when encoders save time-stamps at capture time, when the time stamps propagate with associated coded data to decoders, and when decoders use those time-stamps to schedule presentations.

Synchronization of a decoding system with a data source is achieved through the use of the SCR in the Program Stream and by the equivalent PCR in the Transport Stream. The SCR and PCR are time stamps encoding the timing of the bit stream itself in terms of the same time base as is used for the audio and video PTS values from the same program. Since each program may have its own time base, there are separate PCR fields for each program in a Transport Stream containing multiple programs. It is possible to have only one PCR for some or all programs in a multi-program transport. See clause 2.4.4 on page 30, Program Specific Information (PSI), for the method of identifying which PCR is associated with a program. A program shall have one and only one PCR time base associated with it. Multiple programs may share a common set of PCRs.

0.8.3	Relation to compression layer

0.8.3

The PES packet layer is independent of the compression layer in some senses, but not in all. It is independent in the sense that PES packet payloads need not start at compression layer start codes, as defined in parts 2 and 3 of this Recommendation | International Standard. For example, a video packet may start at any byte in the video stream.  However, time stamps encoded in PES packet headers apply to presentation times of compression layer constructs (namely, presentation units).

0.9	System reference decoder

0.9

Part 1 of ISO/IEC 13818 employs a "System Target Decoder," (STD), one for Transport Streams (see clause 2.4.2 on page 11) referred to as "Transport- System Target Decoder"(T-STD) and one for Program Streams (see clause 2.5.2 on page 41) referred to as "Program -System Target Decoder"(P-STD), to provide a formalism for timing and buffering relationships.  Because the STD is parameterized in terms of ISO/IEC 13818 fields (for example, buffer sizes) each ISO/IEC 13818 stream leads to its own parameterization of the STD. It is up to encoders to ensure that bit streams they produce will forward play in normal speed on corresponding STDs.  Physical decoders may assume that a stream plays properly on its STD; the physical decoder must compensate for ways in which its design differs from that of the STD.

0.10	Applications

0.10

The streams defined in this document are intended to be as useful as possible to a wide variety of applications. Application developers will simply select the most appropriate stream.

Modern data communications networks may be capable of supporting ISO/IEC 13818 audio and video.  A real time transport protocol is required.  The Program Stream may be suitable for transmission on such networks.

The Program Stream is also suitable for multimedia applications on CD-ROM.  Software processing of the Program Stream may be appropriate.

The Transport Stream may be more suitable for error-prone environments, such as those used for

distributing compressed bit-streams over long distance networks and in broadcast systems.

Many applications require storage and retrieval of ISO/IEC 13818 bitstreams on various digital storage media (DSM). A Digital Storage Media Command and Control (DSM CC) protocol is specified in Annex A of this Recommendation | International Standard in order to facilitate the control of such media.

Information technology -- Coding of moving pictures and associated audio

Systems

Section 1: General

1.1	Scope

1.1

This part of ISO/IEC 13818 specifies the system layer of the coding. It was developed principally to support the combination of the video and audio coding methods defined in Parts 2 and 3 of this Recommendation | International Standard. The system layer supports five basic functions: 1) the synchronization of multiple compressed streams on decoding, 2) the interleaving of multiple compressed streams into a single stream, 3) the initialization of buffering for decoding start up, 4) continuous buffer management,  and 5) time identification.

An ISO/IEC 13818 multiplexed bit stream is either a Transport Stream or a  Program Stream. Both streams are constructed from PES packets and packets containing other necessary information. Both streams support multiplexing of video and audio compressed streams from one program with a common time base. The Transport Stream additionally supports the multiplexing of video and audio compressed streams from multiple programs with independent time bases. For almost error-free environments the Program Stream is generally more appropriate, supporting software processing of program information. The Transport Stream is more suitable for use in environments where errors are likely.

An ISO/IEC 13818 multiplexed bit stream, whether a Program Stream or a Transport Stream,  is constructed in two layers: the outermost layer is the system layer, and the innermost is the compression layer. The system layer provides the functions necessary for using one or more compressed data streams in a system. The video and audio parts of this specification define the compression coding layer for audio and video data. Coding of other types of data is not defined by the specification, but is supported by the system layer provided that the other types of data adhere to the constraints defined in clause 2.5.7 on page 69 of this part.

1.2	References

1.2

The following standards contain provisions which, through reference in this text, constitute provisions of this Recommendation | International Standard.  At the time of publication, the editions indicated were valid.  All standards are subject to revision, and parties to agreements based on this Recommendation | International Standard are encouraged to investigate the possibility of applying the most recent editions of the standards indicated below.  Members of IEC and ISO maintain registers of currently valid Recommendation | International Standards.

ISO/IEC 11172-1:1993 Information technology - Coding of moving pictures and associated audio for digital storage media at up to about 1,5 Mbit/s - Part 1: Systems.

ISO/IEC 11172-2:1993 Information technology - Coding of moving pictures and associated audio for digital storage media at up to about 1,5 Mbit/s - Part 2: Video.

ISO/IEC 11172-3:1993 Information technology - Coding of moving pictures and associated audio for digital storage media at up to about 1,5 Mbit/s - Part 3 Audio.

ISO/IEC 13818-2:1994 Information technology - Coding of moving pictures and associated audio - Part 2: Video.

ISO/IEC 13818-3:1994 Information technology - Coding of moving pictures and associated audio - Part 3 Audio.

CCIR Recommendation 601-2 Encoding parameters of digital television for studios.

CCIR Report 624-4 Characteristics of systems for monochrome and colour television.

CCIR Recommendation  648 Recording of audio signals.

CCIR Report 955-2 Sound broadcasting by satellite for portable and mobile receivers, including Annex IV Summary description of Advanced Digital System II.

CCITT Recommendation J.17  Pre-emphasis used on Sound-Programme Circuits.

IEEE Standard 1180-1990 Standard Specification for the Implementations of 8 by 8 Inverse Discrete Cosine Transform

IEC Publication 908:198, CD Digital Audio System

ISO/CD 13522;1993 Information Technology - Coded Representation of Multimedia and Hypermedia Information Objects. (MHEG)

ISO/CD 639-2, Terminology - Code for Presentation of Names of Languages Part 2 Alpha-3 CodeISO 639  Coding of Language Descriptors

2	TECHNICAL ELEMENTS

2.1	Definitions

2.1

For the purposes of this Recommendation | International Standard, the following definitions apply. If specific to a Part, this is parenthetically noted

2.1.1 access unit [system]:  A coded representation of a presentation unit. In the case of compressed audio an access unit is an Audio Access Unit.  In the case of compressed video an access unit is the coded representation of a picture.

2.1.2 bitrate: The rate at which the compressed bit stream is delivered from the storage medium or data-link to the input of a decoder.

2.1.3 byte aligned: A bit in a coded bit stream is byte-aligned if its position is a multiple of 8-bits from the first bit in the stream.

2.1.4 channel: A digital medium that stores or transports an ISO/IEC 13818 stream.

2.1.5 coded representation: A data element as represented in its encoded form.

2.1.6 compression: Reduction in the number of bits used to represent an item of data.

2.1.7 constant bitrate: Operation where the bitrate is constant from start to finish of the compressed bit stream.

2.1.8 constrained system parameter stream (CSPS) [system]: An ISO/IEC 13818 Transport Stream or Program Stream for which the constraints defined in Part 1clause Error! Reference source not found. on page 63 apply.

2.1.9 CRC:  The Cyclic Redundancy Check to verify the correctness of data.

2.1.10 data element: An item of data as represented before encoding and after decoding.

2.1.11 decoded stream: The decoded reconstruction of a compressed bit stream.

2.1.12 decoder: An embodiment of a decoding process.

2.1.13 decoding (process): The process defined in this Recommendation | International Standard that reads an input coded bit stream and outputs decoded pictures or audio samples.

2.1.14 decoding time-stamp; DTS [system]: A field that may be present in a PES packet header that indicates the time that an access unit is decoded in the system target decoder.

2.1.15 digital storage media; DSM: A digital storage or transmission device or system.

2.1.16 entitlement control message; ECM: Entitlement Control Messages are private conditional access information which specify control words and possibly other, typically stream-specific, scrambling and and/or control parameters.

2.1.17 entitlement management message; EMM: Entitlement Management Messages are private conditional access information which specify the authorization levels or the services of specific decoders. They may be addressed to single decoders or groups of decoders.

2.1.18 editing: The process by which one or more compressed bit streams are manipulated to produce a new compressed bit stream.  Conforming edited bit streams must meet the requirements defined in this Recommendation | International Standard.

2.1.19 elementary stream; ES [system]: A generic term for one of the coded video, coded audio or other coded bit streams.

2.1.20 encoder: An embodiment of an encoding process.

2.1.21 encoding (process): A process, not specified in this Recommendation | International Standard, that reads a stream of input pictures or audio samples and produces a valid coded bit stream as defined in this Recommendation | International Standard.

2.1.22 entropy coding: Variable length lossless coding of the digital representation of a signal to reduce redundancy.

2.1.23 fast forward playback [video]: The process of displaying a sequence, or parts of a sequence, of pictures in display-order faster than real-time.

2.1.24 forbidden: The term "forbidden", when used in the clauses defining the coded bit stream, indicates that the value shall never be used.  This is usually to avoid emulation of start codes.

2.1.25 ISO/IEC 13818 (multiplexed) stream [system]: A bit stream composed of  0 or more elementary streams combined in the manner defined in Part 1 of this Recommendation | International Standard.

2.1.26 layer [video and systems]: One of the levels in the data hierarchy of the video and  system specifications defined in Parts 1 and 2 of this Recommendation | International Standard.

2.1.27 pack [system]: A pack consists of a pack header followed by zero or more packets.  It is a layer in the system coding syntax described in clause 2.5.3.3 on page 44 this Recommendation | International Standard.

2.1.28 packet [system]: A packet consists of a header followed by a number of contiguous bytes from an elementary data stream.  It is a layer in the system coding syntax described in clause 2.4.3.6 on page 21 this Recommendation | International Standard.

2.1.29 packet data [system]: Contiguous bytes of data from an elementary stream present in a packet.

2.1.30 packet identifier; PID [system]: A unique integer value used to associate elementary streams of a program in a single or multi-program Transport Stream as described in clause 2.4.3 on page 16.

2.1.31 padding [audio]: A method to adjust the average length of an audio frame in time to the duration of the corresponding PCM samples, by conditionally adding a slot to the audio frame.

2.1.32 PES [system]: An abbreviation for Packetized Elementary Stream.

2.1.33 PES packet [system]:  The data structure used to carry elementary stream data. It consists of a PES packet header followed by PES packet payload and is described in clause 2.4.3.6 on page 21.

2.1.34 PES Stream [system]:  A PES Stream consists of PES packets, all of whose payloads consist of data from a single elementary stream, and all of which have the same stream_id. Specific semantic constraints apply.

2.1.35 presentation time-stamp; PTS [system]:  A field that may be present in a PES packet header that indicates the time that a presentation unit is presented in the system target decoder.

2.1.36 presentation unit; PU [system]: A decoded Audio Access Unit or a decoded picture.

2.1.37 program [system]: A program is a collection of elementary streams with a common time base.

2.1.38 Program Specific Information; PSI [system]: PSI consists of normative data which is necessary for the demultiplexing of Transport Streams and the successful regeneration of programs and is described in clause 2.4.4 on page 30. One case of PSI, the non-mandatory network information table, is privately defined.

2.1.39 random access: The process of beginning to read and decode the coded bit stream at an arbitrary point.

2.1.40 reserved: The term "reserved", when used in the clauses defining the coded bit stream, indicates that the value may be used in the future for ISO defined extensions. Unless otherwise specified within this Recommendation | International Standard, all reserved bits shall be set to '1'.

2.1.41 source stream: A single non-multiplexed stream of samples before compression coding.

2.1.42 start codes [system]: 32-bit codes embedded in the coded bit stream that are unique.  They are used for several purposes including identifying some of the layers in the coding syntax. Start code consists of a 24 bit prefix (0x0000001) and an 8 bit stream_id as shown in table 2-24 on page 49

2.1.43 STD input buffer [system]: A first-in first-out buffer at the input of system target decoder for storage of compressed data from elementary streams before decoding.

2.1.44 still picture: A coded still picture consists of a video sequence containing exactly one coded picture which is intra-coded. This picture has an associated PTS and the presentation time of succeeding pictures, if any, is later than that of the still picture by at least two picture periods.

2.1.45 system header [system]:  The system header is a data structure defined in clause 2.5.3.5 on page 46 of this Recommendation | International Standard that carries information summarizing the system characteristics of the ISO/IEC 13818 multiplexed stream.

2.1.46 system target decoder; STD [system]: A hypothetical reference model of a decoding process used to describe the semantics of an ISO/IEC 13818 multiplexed bit stream.

2.1.47 time-stamp [system]: A term that indicates the time of an event.

2.1.48 Transport Stream packettransport packet header [system]: A data structure used to convey information about the Transport Stream payload.

2.1.49 variable bitrate: Operation where the bitrate varies with time during the decoding of a compressed bit stream.

2.2	Symbols and abbreviations

2.2

The mathematical operators used to describe this Recommendation | International Standard are similar to those used in the C programming language.  However, integer division with truncation and rounding are specifically defined.  The bitwise operators are defined assuming two's-complement representation of integers.  Numbering and counting loops generally begin from 0.

2.2.1	Arithmetic operators

2.2.1

+	Addition.

-	Subtraction (as a binary operator) or negation (as a unary operator).

++	Increment.

- -	Decrement.

* or 	Multiplication.

^	Power.

/	Integer division with truncation of the result toward 0.  For example, 7/4  and -7/-4 are truncated to 1 and -7/4 and 7/-4 are truncated to -1.

//	Integer division with rounding to the nearest integer.  Half-integer values are rounded away from 0 unless otherwise specified.  For example 3//2 is rounded to 2, and -3//2 is rounded to 
-2.

DIV	Integer division with truncation of the result towards -.

%	Modulus operator.  Defined only for positive numbers.

Sign(  )	Sign(x)	=  1	x  > 0

0	x == 0

-1	x  < 0

NINT (  )	Nearest integer operator.  Returns the nearest integer value to the real-valued argument.  Half-integer values are rounded away from 0.

sin	Sine.

cos	Cosine.

exp	Exponential.

Square root.

log10	Logarithm to base ten.

loge	Logarithm to base e.

2.2.2	Logical operators

2.2.2

||	Logical OR.

&&	Logical AND.

!	Logical NOT.

2.2.3	Relational operators

2.2.3

Greater than.

Greater than or equal to.

Less than.

Less than or equal to.

==	Equal to.

!=	Not equal to.

max [,...,]	the maximum value in the argument list.

min [,...,]	the minimum value in the argument list.

2.2.4	Bitwise operators

2.2.4

&	AND.

|	OR.

Shift right with sign extension.

Shift left with 0 fill.

2.2.5	Assignment

2.2.5

=	Assignment operator.

2.2.6	Mnemonics

2.2.6

The following mnemonics are defined to describe the different data types used in the coded bit-stream.

bslbf	Bit string, left bit first, where "left" is the order in which bit strings are written in the Recommendation | International Standard. Bit strings are written as a string of 1s and 0s within single quote marks, e.g. '1000 0001'.  Blanks within a bit string are for ease of reading and have no significance.

ch	channel.

gr	granule of 3 * 32 subband samples in audio Layer II, 18 * 32 sub-band samples in audio Layer III.

main_data	The main_data portion of the bit stream contains the scale factors, Huffman encoded data, and ancillary information.

main_data_beg 	This gives the location in the bit stream of the beginning of the main_data for the frame. The location is equal to the ending location of the previous frame's main_data plus 1 bit. It is calculated from the main_data_end value of the previous frame.

part2_length	this value contains the number of main_data bits used for scale factors.

rpchof	remainder polynomial coefficients, highest order first.

sb	subband.

scfsi	scalefactor selector information.

switch_point_l	Number of scalefactor band (long block scalefactor band) from which point on window switching is used.

switch_point_s	Number of scalefactor band (short block scalefactor band) from which point on window switching is used.

tcimsbf	two's complement integer, msb (sign) bit first.

uimsbf	Unsigned integer, most significant bit first.

vlclbf	Variable length code, left bit first, where "left" refers to the order in which the VLC codes are written.

window 	Number of actual time slot in case of block_type==2, 0  window  2.

The byte order of multi-byte words is most significant byte first.

2.2.7	Constants

2.2.7

3.14159265359

e	2.71828182845

2.3	Method of describing bit stream syntax

2.3

The bit streams retrieved by the decoder are described in clause 2.4.1 on page 9 and clause 2.5.1 on page 40. Each data item in the bit stream is in bold type.  It is described by its name, its length in bits, and a mnemonic for its type and order of transmission.

The action caused by a decoded data element in a bit stream depends on the value of that data element and on data elements previously decoded.  The decoding of the data elements and definition of the state variables used in their decoding are described in the clauses containing the semantic description of the syntax. The following constructs are used to express the conditions when data elements are present, and are in normal type:

Note this syntax uses the "C"-code convention that a variable or expression evaluating to a non-zero value is equivalent to a condition that is true.

while ( condition ) {

data_element

. . .

| } | If the condition is true, then the group of data elements occurs next in the data stream. This repeats until the condition is not true. |  |
| --- | --- | --- |

do {

data_element

| . . . | The data element always occurs at least once. |  |
| --- | --- | --- |

} while ( condition )

if ( condition)  {

data_element

. . .

| } | The data element is repeated until the condition is not true. If the condition is true, then the first group of data elements occurs next in the data stream. |  |
| --- | --- | --- |

else  {

data_element

. . .

| } | If the condition is not true, then the second group of data elements occurs next in the data stream. |  |
| --- | --- | --- |

for (i = 0,i<n,i++) {

data_element

. . .

| } | The group of data elements occurs n times. Conditional constructs within the group of data elements may depend on the value of the loop control variable i, which is set to zero for the first occurrence, incremented to 1 for the second occurrence, and so forth. |  |
| --- | --- | --- |

As noted, the group of data elements may contain nested conditional constructs.  For compactness, the {} are omitted when only one data element follows.

data_element []

data_element [] is an array of data. The number of data elements is indicated by the context.

|  |  | data_element [n] |
| --- | --- | --- |

data_element [n] is the n+1th element of an array of data.

|  |  | data_element [m][n] |
| --- | --- | --- |

data_element [m][n] is the m+1,n+1 th element of a two-dimensional array of data.

|  |  | data_element [l][m][n] |
| --- | --- | --- |

data_element [l][m][n] is the l+1,m+1,n+1 th element of a three-dimensional array of data.

|  |  | data_element [m..n] |
| --- | --- | --- |

is the inclusive range of bits between bit m and bit n in the data_element.

While the syntax is expressed in procedural terms, it should not be assumed that either figure 2-6 on page 11  or figure 2-7 on page 41 implements a satisfactory decoding procedure.  In particular, they define a correct and error-free input bitstream. Actual decoders must include a means to look for start codes and sync bytes (Transport Stream) in order to begin decoding correctly, and to identify errors, erasures or insertions while decoding. The methods to identify these situations, and the actions to be taken, are not standardized.

Definition of bytealigned function

The function bytealigned () returns 1 if the current position is on a byte boundary, that is the next bit in the bit stream is the first bit in a byte.  Otherwise it returns 0.

Definition of nextbits function

The function nextbits () permits comparison of a bit string with the next bits to be decoded in the bit stream.

Definition of next_start_code function

The next_start_code function removes any zero bit and zero byte stuffing and locates the next start code.

Table 2-1 -- Next start code2-1

| Syntax | No. of bits | Mnemonic |  | next_start_code() { |  |  |  | while ( !bytealigned() ) |  |  |  | zero_bit | 1 | '0' |  | while ( nextbits() != '0000 0000 0000 0000 0000 0001' ) |  |  |  | zero_byte | 8 | '00000000' |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

This function checks whether the current position is byte aligned.  If it is not, 0 stuffing bits are present.  After that any number of 0 bytes may be present before the start-code.  Therefore start-codes are always byte aligned and may be preceded by any number of 0 stuffing bits.

2.4	Transport Stream bitstream requirements

2.4

2.4.1 	Transport Stream coding structure and parameters

2.4.1

The Transport Stream coding layer allows one or more groups of one or more elementary streams to be combined into a single stream. A group of elementary streams, with a common system_clock_frequency time base, is called a program. Data from each elementary stream are encoded and multiplexed together with information that allows elementary streams within a program to be replayed in synchronism.

ISO/IEC 13818 multiplexed Transport Stream

An ISO/IEC 13818 Transport Stream consists of one or more programs each containing one or more elementary streams and other streams multiplexed together. Each elementary stream consists of access units, which are the coded representation of presentation units.  The presentation unit for a video elementary stream is a picture.  The corresponding access unit includes all the coded data for the picture. If the picture is the first of a group of pictures (GOP) then the access unit also includes any preceeding data from that GOP starting with the first byte of the group_start_code. Group_start_code is defined in part 2 of this Recommendation | International Standard. If the picture is the first coded picture after a sequence header, then the access unit also includes the sequence header starting with the first byte of the sequence_header_code.  Sequence_header_code is defined in part 2 of this Recommendation | International Standard. Otherwise a video access unit commences with the first byte of a picture_start_code which is defined in part 2 of this Recommendation | International Standard.  The sequence_end_code is included in the Access Unit containing the last coded picture of a sequence.  (See Part 2 of this Recommendation | International Standard for the definition of the sequence_end_code).  The presentation unit for an audio elementary stream is the set of samples that corresponds to samples from an audio frame. The corresponding audio access unit commences with the first byte of the audio frame synchronization word. (see Part 3 of this Recommendation | International Standard for the definition of an audio frame).

Elementary Stream data is carried in PES packets. A PES packet consists of a PES packet header followed by packet data. PES packets are inserted into Transport Stream packettransport packets. The first byte of each PES packet header is located at the first available payload  location of a Transport Stream packettransport packet.

The PES packet header begins with a 32-bit start-code that also identifies the stream to which the packet data belongs.  The PES packet header may contain decoding and/or presentation time-stamps (DTS and PTS) that refer to the first access unit that commences in the packet. The PES packet header also contains a number of flags opening up a range of optional fields. The packet data contains a variable number of contiguous bytes from one elementary stream.

Transport Stream packetTransport packets begin with a 4 byte prefix, which contains a 13 bit Packet ID (PID), defined in table 2-3 on page 17 . The PID identifies, via the Program Specific Information (PSI) tables, the contents of the data contained in the Transport Stream packettransport packet. Transport Stream packetTransport packets of one PID value carry data of one and only one elementary stream.

The PSI tables are carried in the Transport Stream. There are four PSI tables:

Program Association Table

Program Map Table

Network Information Table

Conditional Access Table

These tables contain the necessary and sufficient information to demultiplex and present programs.  The Program Map Table, in table 2-18 on page 37 , specifies, among other information, which PIDs, and therefore which elementary streams are associated to form each program. This table also indicates the PID of the Transport Stream packettransport packets which carry the PCR for each program.

Transport Stream packets may be null packets. Null packets are intended for padding of Transport Streams. They may be inserted or deleted by re-multiplexing processes and, therefore, the delivery of the payload of null packets to the decoder cannot be assumed.

This standard does not specify the coded data which may be used as part of conditional access systems.  The standard does however provide mechanisms for program service providers to transport and identify this data for decoder processing, and to reference correctly data which are specified by the standard. This type of support is provided both through Transport Stream packettransport packet structures and in the conditional access table (see table 2-17 on page 35  of the PSI.

2.4.2	Transport Stream system target decoder

2.4.2

The semantics of the Transport Stream specified in clause 2.4.3 on page 16 and the constraints on these semantics specified in clause 2.5.7 on page 69 require exact definitions of decoding events and the times at which these events occur.  The definitions needed are set out in this Recommendation | International Standard using a hypothetical decoder known as the Transport Stream system target decoder (T-STD).

The T-STD is a conceptual model used to define these terms precisely and to model the decoding process during the construction of ISO/IEC 13818 Transport Streams. The T-STD is defined only for this purpose.  Neither the architecture of the T-STD nor the timing described precludes uninterrupted, synchronized play-back of ISO/IEC 13818 Transport Streams from a variety of decoders with different architectures or timing schedules.

Figure 2-6 -- ISO/IEC 13818 Transport Stream system target decoder notation2-6

The following notation is used to describe the Transport Stream system target decoder and is partially illustrated in figure 2-6 above.

i, i', i"	are indices to bytes in the ISO/IEC 13818 Transport Stream.  The first byte has index 0.

j	is an index to access units in the elementary streams.

k, k',k''	are indices to presentation units in the elementary streams.

n	is an index to the elementary streams.

p	is an index to Transport Stream packettransport packets in the ISO/IEC 13818 Transport Stream

M(i)	is the ith byte in the Transport Stream.

tm(i)	indicates the time in seconds at which the ith byte of the ISO/IEC 13818 Transport Stream enters the system target decoder.  The value tm(0) is an arbitrary constant.

PCR(i)	is the time encoded in the PCR field measured in units of the 27 MHz system clock where i is the byte index of the final byte of the PCR field.

An(j)	is the jth access unit in elementary stream n.  Note that access units are indexed in decoding order.

tdn(j)	is the decoding time, measured in seconds, in the system target decoder of the jth access unit in elementary stream n.

tbn(p)	indicates the time, measured in seconds, at which the pth Transport Stream packettransport packet of the Mth Transport Stream enters buffer Bn.

tbsys(p)	indicates the time, measured in seconds, at which the pth Transport Stream packettransport packet of the Mth Transport Stream enters buffer Bsys.

Pn(k)	is the kth presentation unit in elementary stream n.

tpn(k)	is the presentation time, measured in seconds, in the system target decoder of the kth presentation unit in elementary stream n.

t	is time measured in seconds.

Fn(t)	is the fullness, measured in bytes, of the system target decoder input buffer for elementary stream n at time t.

Bn	the main buffer in the system target decoder for elementary stream n.

BSn	is the size of the system target decoder main buffer, measured in bytes, for elementary stream n.

Bsys	is the main buffer in the system target decoder for system information for the program that is in the process of being decoded.

BSsys	is the size of the main buffer in the system target decoder, measured in bytes, for system information for the program that is in the process of being decoded.

TBsys	is the input buffer in the system target decoder for system information for the program that is in the process of being decoded.

TBSsys	is the size of the input buffer in the system target decoder, measured in bytes, for system information for the program that is in the process of being decoded.

TBn	the transport buffer in the system target decoder for elementary stream n.

TBSn	is the size of the system target decoder transport buffer, measured in bytes, for elementary stream n.

Ttp	indicates the length of the period during which one Transport Stream packettransport packet arrives at the input of the system target decoder.

Dsys	is the decoder for system information in Program Stream n.

Dn	is the decoder for elementary stream n.

On	is the reorder buffer for video elementary stream n.

Rsys	is the rate at which data are removed from Bsys.

Resn	is the rate of the elementary stream n.

Ln	is the latency time after which one half of each Transport Stream packettransport packet enters TBn before that Transport Stream packettransport packet leaves TBn.

System clock frequency

Timing information referenced in T-STD is carried by several data fields defined in this Recommendation | International Standard. Refer to clause 2.4.3.4 on page 19, and clause 2.4.3.6 on page 21. This information is coded as the sampled value of a system clock.

The value of the system clock frequency is measured in Hz and shall meet the following constraints:

27 000 000 - 1 350  system_clock_frequency  27 000 000 + 1 350

rate of change of system_clock_frequency with time  75  10-3  Hz/s

The notation "system_clock_frequency" is used in several places in this Recommendation | International Standard to refer to the frequency of a clock meeting these requirements. For notational convenience, equations in which PCR, PTS, or DTS appear, lead to values of time which are accurate to some integral multiple of (300233/system_clock_frequency). This is due to the encoding of PCR timing information as 33 bits of 1/300 of the system clock frequency plus 9 bits for the remainder, and encoding as 33 bits of the system clock frequency divided by 300 for PTS and DTS.

Input to the Transport Stream system target decoder

Input to the Transport Stream system target decoder (T-STD) is an ISO/IEC 13818 Transport Stream. A Transport Stream may contain multiple programs with independent time bases. However, the T-STD decodes only one program at a time. In the T-STD model all timing indications refer to the time base of that program.

Data from the ISO/IEC 13818 Transport Stream enters the system target decoder at a piece-wise constant rate. The ith byte, M(i), enters at time tm(i).  The time at which this byte enters the system target decoder can be recovered from the input stream by decoding the input program clock reference (PCR) fields, encoded in the Transport Stream packettransport packet adaptation field, of the program to be decoded.  The PCR is encoded in equation 2-3 in  two parts; one, in units of 1/300 times the system clock frequency, called PCR_base(equation 2-1 ), and one, called PCR_ext (equation 2-2 ), in units of the system clock frequency. The value encoded in the PCR(i') field indicates time tm(i'), where i' refers to the byte containing the last bit  of the PCR_base field, M(i').

Specifically:

(2-1)
2-1

(2-2)
2-2

(2-3)
2-3

The input arrival time, tm(i) is shown in equation 2-4 below, for all other bytes shall be constructed from PCR(i') and the transport rate at which data arrive, where the transport rate is determined as the number of bytes in the Transport Stream between the bytes containing the last bit of two successive PCR fields of the same program divided by the difference between the time values encoded in these same two PCR fields.

(2-4)
2-4

Where:

i''	is the index of the byte containing the last bit of the program_clock_reference base field in the Transport Stream packettransport packet adaptation field.

i	is the index of any byte in the Transport Stream.

PCR(i")	is the time encoded in the program_clock_reference base and extension fields in units of the system clock.

(2-5)
2-5

where

i''	is the index of the byte containing the last bit of the latest program_clock_reference base preceding the PCR_base field at i', in the Transport Stream packettransport packet with the same PID as that containing i'.

and	i"   i    i'

Buffering

Complete Transport Stream packettransport packets containing data from elementary stream n, as indicated in the PID, are passed to the transport buffer for stream n, TBn.  Transfer of byte M(i) from the system target decoder input to TBn is instantaneous, so that byte M(i) enters the buffer for stream n, of size TBSn, at time tm(i).

Bytes present in the Transport Stream packettransport packet, which are part of the PES packet or its contents are delivered to the main buffer Bn. Other bytes are not, and may be used to control the system.

Each complete Transport Stream packettransport packet which has entered TBn is removed instantaneously and immediately placed in Bn at the time specified as latency Ln following the time when one-half of the Transport Stream packettransport packet has entered TBn. The value of Ln is defined in equation 2-6 below. The Transport Stream packettransport packet time Ttp is 188 divided by the Transport Stream rate in bytes per second, as calculated above using the Program Clock Reference (PCR). Each byte of each Transport Stream packettransport packet is moved from TBn to Bn at the specified time if and only if there is space available in Bn. If there is no space in Bn the remaining Transport Stream packettransport packet data bytes remains in TBn; these remaining bytes are moved as soon as space is available in Bn.

Each elementary stream has a maximum elementary stream rate Res(max), which is indicated within the bit streams which are specified in Parts 2 and 3 of this Recommendation | International Standard. In the case of constant bitrate operations Res(max)  Res. The latency Ln is specified by the following:

then

else

(2-6)
2-6

Note -

Complete Transport Stream packettransport packets containing system information, for the program selected for decoding, enter the system transport buffer, TBsys, at the Transport Stream rate. These include Transport Stream packettransport packets whose PID values are 0 or 1, and all Transport Stream packettransport packets identified via the Program Association Table (table 2-15 on page 33 )as having the PMT_PID value for the selected program.

The transport buffer size is fixed at 512 bytes.

The main buffer sizes BS1 through BSn are defined as follows. In the case of constant bitrate operations Res(max)  Res. A theoretical effective rate Reff is calculated as the elementary stream rate, Res(max), multiplied by 188/184. A portion BSmux of the buffer size BSn allocated for multiplex buffering is defined as BSmux = Reff  4 milliseconds. Another portion, BSn(dec), of the buffer size allocated for decoding is the size of the Video Buffering Verifier, as specified in Part 2 of this Recommendation | International Standard, in the case of video elementary stream data, or the size of one audio access unit, equivalently a coded audio frame, as specified in Part 3 of this Recommendation | International Standard, in the case of audio elementary stream data. The size BSn of buffer Bn is equal to the sum BSmux + BSn(dec).

The main buffer Bsys for system data  is of size BSsys = 1536 bytes.

For each elementary stream buffer, all the data for the access unit that has been in the input buffer, An(j), longest is removed instantaneously at its decoding time tdn(j).  In the case of an ISO/IEC 13818 video stream the decoding time, tdn(j), may be derived from subclauses C.9 to C.11 of annex C of ISO/IEC 13818-2.  The data defined as belonging to an ISO/IEC 13818 video access unit for this purpose is defined in subclause C.5  of annex C of ISO/IEC 13818-2.  In the case of an ISO/IEC 13818 audio stream, access units consist of audio frames.  All PES packet headers that are stored immediately before the access unit or that are embedded within the data of the access unit are removed simultaneously with the removal of the access unit.  As the access unit is removed it is instantaneously decoded to a presentation unit.

When the low_delay flag in the video sequence extension is set to '1' (subclause 6.2.2.3 of ISO/IEC 13818-2) the VBV buffer may underflow.  In this case when the T-STD elementary stream buffer Bn is examined at the time specified by tdn(j), the complete data for the access unit may not be present in the buffer Bn.  When this case arises, the buffer shall be re-examined at intervals of two field-periods until the data for the complete access unit is present in the buffer.  At this time the entire access unit and associated system data if any shall be removed from buffer Bn instantaneously.  Overflow of buffer Bn shall not occur.

VBV buffer underflow is allowed to occur continuously without limit.  The T-STD decoder shall remove access unit data from buffer Bn at the earliest time consistent with the paragraph above and any DTS or PTS values encoded in the bitstream.  Note that the decoder may be unable to re-establish correct decoding and display times as indicated by DTS and PTS until the VBV buffer underflow situation ceases and a PTS or DTS is found in the bitstream.

In the case of system data, data is removed from the main buffer Bsys at a rate of Rsys  whenever there is at least 1 byte available in buffer Bsys.

(2-7)

The intention of increasing Rsys in the case of high transport rates is to allow an increased data rate for the Program Association Table.

2-7

Decoding

Elementary streams buffered in B1 through Bn are decoded instantaneously by decoders D1 through Dn and may be delayed in reorder buffers O1 through On before being presented to the viewer at the output of the system target decoder. Reorder buffers are used only in the case of a video elementary stream when some access units are not carried in presentation order. These access units will need to be reordered before presentation. In particular, if Pn(k) is an I-picture or a P-picture carried before one or more B-pictures, then it must be delayed in the reorder buffer, On, of the T-STD before being presented. Any picture previously stored in On is presented before the current picture can be stored. Pn(k) should be delayed until the next I-picture or P-picture is decoded. While it is stored in the reorder buffer, the subsequent B-pictures are decoded and presented.

The time at which a presentation unit Pn(k) is presented to the viewer is tpn(k). For presentation units that do not require reordering delay, tpn(k) is equal to tdn(j) since the access units are decoded instantaneously; this is the case, for example, for B-frames. For presentation units that are delayed tpn(k) and tdn(j) differ by the time that Pn(k) is delayed in the reorder buffer, which is a multiple of the nominal picture period. Care should be taken to use adequate re-ordering delay from the beginning of video elementary streams to meet the requirements of the entire stream. For example, a stream which initally has only I- and P-pictures but later includes B-pictures should include re-ordering delay starting at th beginning of the stream.

Part 2 of this Recommendation | International Standard explains reordering of video pictures in greater detail.

Presentation

The function of a decoding system is to reconstruct presentation units from compressed data and to present them in a synchronized sequence at the correct presentation times. Although real audio and visual presentation devices generally have finite and different delays and may have additional delays imposed by post-processing or output functions, the system target decoder models these delays as zero.

In the T-STD in figure 2-6 on page 11 the display of a video presentation unit (a picture) occurs instantaneously at its presentation time, tpn(k).

In the T_STD the output of an audio presentation unit starts at its presentation time, tpn(k), when the decoder instantaneously presents the first sample. Subsequent samples in the presentation unit are presented in sequence at the audio sampling rate.

2.4.3	Specification of the Transport Stream syntax and semantics

2.4.3

The following syntax describes a stream of bytes.

2.4.3.1 ISO/IEC 13818 Transport Stream

2.4.3.1

Table 2-2 -- ISO/IEC 13818 Transport Stream2-2

| Syntax | No. of bits | Mnemonic |  | MPEG_transport_stream() { |  |  |  | do { |  |  |  | transport_packet() |  |  |  | } while (nextbits() == sync_byte) |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.3.2 Transport Stream packet layer

2.4.3.2

Table 2-3 -- ISO/IEC 13818 transport header2-3

| Syntax |  | No. of bits | Mnemonic |  | transport_packet(){ |  |  |  |  | sync_byte |  | 8 | bslbf |  | transport_error_indicator |  | 1 | bslbf |  | payload_unit_start_indicator |  | 1 | bslbf |  | transport_priority |  | 1 | bslbf |  | PID |  | 13 | uimsbf |  | transport_scrambling_control |  | 2 | bslbf |  | adaptation_field_control |  | 2 | bslbf |  | continuity_counter |  | 4 | uimsbf |  | if(adaptation_field_control=='10' ¦¦ adaptation_field_control=='11'){ |  |  |  |  | adaptation_field() |  |  |  |  | } |  |  |  |  | if(adaptation_field_control=='01' ¦¦ adaptation_field_control=='11') { |  |  |  |  | for (i=0;i<N;i++){ |  |  |  |  | data_byte |  | 8 | bslbf |  | } |  |  |  |  | } |  |  |  |  | } |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.3.3 Semantic definition of fields in Transport Stream packet layer

2.4.3.3

sync_byte -- The sync byte is a fixed 8 bit field whose value is '0100 0111' (0x47).

transport_error_indicator -- The transport_error_indicator is a 1 bit flag. When set to '1' it indicates that at least 1 uncorrectable bit error exists in the associated Transport Stream packet. This bit may be set to a value of '1' by entities external to the transport layer. When set to a value of '1' this bit shall not be reset to a value of  '0' unless the bit value(s) in error have been corrected.

payload_unit_start_indicator -- The payload_unit_start_indicator is a 1 bit flag which has normative meaning for Transport Stream packets that carry PES packets or PSI data.

When the payload of the Transport Stream packet contains PES packet data, the payload_unit_start_indicator has the following significance: A '1' indicates that the payload of this Transport Stream packet will commence with the first byte of a PES packet and a '0' indicates no PES packet shall start in this Transport Stream packet. One and only one PES packet may start in any Transport Packet. This also applies to private streams of stream_type 6(refer to table 2-26 on page 52).

When the payload of the Transport Stream packet contains PSI data, the payload_unit_start_indicator has the following significance: If the Transport Stream packet carries the first byte of a PSI section, the payload_unit_start_indicator value shall be '1', indicating that the first byte of the payload of this Transport Stream packet carries the pointer_field. If the Transport Stream packet does not carry the first byte of a PSI section, the payload_unit_start_indicator value shall be '0', indicating that there is no pointer_field in the payload. Refer to clause 2.4.4.1 and clause 2.4.4.2 on page 31. This also applies to private streams of stream_type 5(refer to table 2-26 on page 52).

For null packets the payload_unit_start_indicator shall be set to '0'.

The meaning of this bit for Transport Stream packets carrying only private data is not defined in this Recommendation | International Standard.

transport_priority -- The transport_priority is a 1 bit indicator. When set to '1' it indicates that the associated packet is of greater priority than other packets having the same PID which do not have the bit set to '1'. The transport mechanism can use this to prioritize its data within an elementary stream. Depending on the application the priority field may be coded regardless of the PID or within one PID only. This field may be changed by data link specific encoders or decoders.

PID -- The PID is a 13 bit field, indicating the type of the data stored in the packet payload. PID value 0x0000 is reserved for the Program Association Table(table 2-15 on page 33 ). PID value 0x0001 is reserved for Conditional Access Table (table 2-17 on page 35 ). PID values 0x0002-0x000F are reserved. PID value 0x1FFF is reserved for null packets.

transport_scrambling_control -- This 2 bit field indicates the scrambling of the Transport Stream packet payload. The Transport Stream packet header, including the adaptation field when present, shall not be scrambled. In the case of a null packet the value of the transport_scrambling_control field shall be set to '00'.

Table 2-4 -- Scrambling control values2-4

| value | Description |  | 00 | not scrambled |  | 01 | user defined |  | 10 | user defined |  | 11 | user defined |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

adaptation_field_control -- This 2 bit field indicates whether this Transport Stream packet header is followed by an adaptation field and/or payload.

Table 2-5 -- Adaptation field control values2-5

| value | Description |  | 00 | reserved for future use by ISO/IEC |  | 01 | no adaptation_field, payload only |  | 10 | adaptation_field only, no payload |  | 11 | adaptation_field followed by payload |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

ISO/IEC 13818 decoders shall discard Transport Stream packets with the adaptation_field_control field set to a value of '00'. In the case of a null packet the value of the adaptation_field_control shall be set to '01'.

continuity_counter -- The continuity_counter is a 4 bit field incrementing with each Transport Stream packet with the same PID. The continuity_counter wraps around to 0 after its maximum value. The continuity_counter shall not be incremented when the adaptation_field_control of the packet equals '00' or '10'. In ISO/IEC 13818 Transport Streams, duplicate packets may be sent as two consecutive Transport Stream packets of the same PID. The duplicate packets shall have the same continuity_counter value as the original packet and the adaptation_field_control field shall be equal to  '01' or '11'. In duplicate packets each byte of the original packet shall be duplicated, with the exception that in the program clock reference fields, if present, a valid value shall be encoded. In the case of a null packet the value of the continuity_counter is undefined.

data_byte -- Data bytes shall be contiguous bytes of data from the PES packets stream, PSI tables sections or private data not in these structures as  indicated by the PID. In the case of null packets with PID value 0x1FFF, all data_bytes shall be stuffing bytes data_bytes may be assigned any value.

2.4.3.4 Adaptation field

2.4.3.4

Table 2-6 -- Transport Stream adaptation field2-6

| Syntax | No. of Bits | Mnemonic |  | adaptation_field() { |  |  |  | adaptation_field_length | 8 | uimsbf |  | if(adaptation_field_length >0) { |  |  |  | discontinuity_indicator | 1 | bslbf |  | random_access_indicator | 1 | bslbf |  | elementary_stream_priority_indicator | 1 | bslbf |  | PCR_flag | 1 | bslbf |  | OPCR_flag | 1 | bslbf |  | splicing_point_flag | 1 | bslbf |  | transport_private_data_flag | 1 | bslbf |  | adaptation_field_extension_flag | 1 | bslbf |  | if(PCR_flag == '1') { |  |  |  | program_clock_reference_base | 33 | uimsbf |  | reserved | 6 | bslbf |  | program_clock_reference_extension | 9 | uimsbf |  | } |  |  |  | if(OPCR_flag == '1') { |  |  |  | original_program_clock_reference_base | 33 | uimsbf |  | reserved | 6 | bslbf |  | original_program_clock_reference_extension | 9 | uimsbf |  | } |  |  |  | if (splicing_point_flag == '1') { |  |  |  | splice_countdown | 8 | tcimsbf |  | } |  |  |  | if(transport_private_data_flag == '1') { |  |  |  | transport_private_data_length | 8 | uimsbf |  | for (i=0; i<transport_private_data_length;i++){ |  |  |  | private_data_byte | 8 | bslbf |  | } |  |  |  | } |  |  |  | if (adaptation_field_extension_flag == '1' ) { |  |  |  | adaptation_field_extension_length | 8 | uimsbf |  | for ( i=0;i<adaptation_field_extension_length;i++) { |  |  |  | reserved | 8 | bslbf |  | } |  |  |  | } |  |  |  | for (i=0;i<N;i++){ |  |  |  | stuffing_byte | 8 | bslbf |  | } |  |  |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.3.5 Semantic definition of fields in adaptation field

2.4.3.5

adaptation_field_length -- The adaptation_field_length is an 8 bit field specifying the number of bytes in the adaptation_field immediately following the adaptation_field_length field. The value '0' is forbidden and tThe length shall not exceed 183 bytes. The value '0' is permitted, to support the stuffing of a single byte at this level.

discontinuity_indicator -- This is a 1 bit field which when set to '1' indicates that the next PCR in a Transport Stream packet with the same PID represents a sample of a new system time clock for the associated program. When there is a discontinuity a Transport Stream packet with the first PCR of the new time-base shall have this bit set to '1'. This bit may also be set in prior packets preceding the discontinuity. When set to a value of '0' no discontinuity in PCR fields shall occur in the following the Transport Stream packets of the same PID value.

random_access_indicator -- The random_access_indicator is a 1 bit field. When set to '1', it indicates that the next PES packet in this Transport Stream packet or in subsequent Transport Stream packets with the same PID shall contain a PTS field and an elementary stream access point. For the purpose of this Clause, an elementary stream access point is defined as follows:

Video:	the first byte of a video sequence header

Audio:	the first byte of an audio frame

In Transport Stream packets where the random_access_indicator is set to a value of '1', there shall be an adaptation field which shall contain at least the program_clock_reference_base and program_clock_reference_extension fields. When set to a value of '0' it is not defined whether a random access point occurs or not. The meaning of the flag is not defined for private data.

elementary_stream_priority_indicator -- The elementary_stream_priority_indicator is a single bit field. It indicates, within this PID, the priority of the elementary stream data carried within the payload of this Transport Stream packet. A '1' indicates that the payload has a higher priority than the payloads of other Transport Stream packets. In case of video this field may be set to '1' only if the payload contains one or more bytes from an intra-coded slice. A value of  '0' indicates that the payload has the same priority as all other packets which do not have this bit set to a value of '1'.

PCR_flag -- The PCR_flag is a 1 bit flag. A '1' indicates that the adaptation_field contains a PCR field. A value of  '0' indicates that the adaptation field does not contain any PCR fields.

OPCR_flag -- The OPCR_flag is a 1 bit flag. A '1' indicates that the adaptation_field contains an OPCR field. A value of  '0' indicates that the adaptation field does not contain any OPCR fields.

splicing_point_flag -- The splicing_point_flag is a 1 bit flag. When set to '1', it indicates that a splice_countdown field shall be present in the associated adaptation field, specifying the occurence of  a splicing point. A value of '0' indicates that a splice_countdown field is not present in the adaptation field.

transport_private_data_flag -- The transport_private_data_flag is a 1 bit flag. A value of  '1' indicates that the adaptation field contains one or more private_data bytes. A value of '0' indicates the adaptation field does not contain any private_data bytes.

adaptation_field_extension_flag -- The adaptation_field_extension_flag is a 1 bit field which when set to '1' indicates the presence of an adaptation field extension. This feature is included to allow for future growth of the adaptation field. A value of  '0' indicates that an adaptation field extension is not present in the adaptation field.

program_clock_reference_base; program_clock_reference_extension -- The program_clock_reference (PCR) as defined in (equation 2-3 on page 13 ), is a 42 bit field coded in two parts; one, in units of 1/300 multiplied by the system clock frequency (90kHz) called program_clock_reference_base (equation 2-1 on page 13 ), is a 33 bit field and one called program_clock_reference_extension (equation 2-2 on page 13 ), is a 9 bit field in units of system clock frequency (27MHz). Its presence is indicated by the PCR_flag. The PCR indicates the intended time of arrival of  the byte containing the last bit of the program_clock_reference_base at the input of the system target decoder.

The program_clock_reference_extension field indicates the number of periods of a 27MHz clock after a 90kHz period start. The value of this field will be between 0 and 299. When the value equals 299, the program_clock_reference_extension will wrap around to zero and simultaneously the lsb (least significant bit) of the program_clock_reference_base field will increment by 1. For Transport Stream packets containing video or audio elementary streams, if a PCR field is present in the adaptation field, that PCR field must be valid for the elementary stream contained in its Transport Stream packettransport packet.

original_program_clock_reference_base;  original_program_clock_reference_extension -- The optional original program clock reference (OPCR) is a 42 bit field coded in two parts; one, in units of 1/300 multiplied by the system clock frequency (90kHz) called original_program_clock_reference_base is a 33 bit field and one called original_program_clock_reference_ext is a 9 bit field in units of system clock frequency (27MHz). OPCR indicates the intended time of arrival of the byte containing the last bit of the original_program_clock_reference_base reference field at the system target decoder in a single program Transport Stream. If it is present in a multi-program Transport Stream, it may be ignored by the decoder. Further, it may not be modified by any multiplexor or decoder. The OPCR use is for recovery of the original single-program Transport Stream with its identical time stamps. The OPCR will only be valid if, e.g. by private arrangements, the original single program Transport Stream is reconstructed exactly.

splice_countdown --The splice_countdown is an 8 bit field, representing a value which may be positive or negative. A positive value specifies the remaining number of Transport Stream packettransport packets, of the same PID,  following the associated Transport Stream packettransport packet until a splicing point is reached. Duplicate Transport Stream packettransport packets and Transport Stream packettransport packets which contain adaptation fields are excluded. The splicing point occurs immediately after the transfer to buffer Bn in the STD model of the Transport Stream packettransport packet in which the splice_countdown reaches the value 0. At the splicing point, the contents of buffer Bn shall be less than or equal to 1/8 of the size BSn of buffer Bn. In the Transport Stream packettransport packet where the splice_countdown value reaches 0, the last byte of the Transport Stream packettransport packet payload shall be the last byte of an access unit. Transport Stream packetTransport packets with the same PID, which follows, may contain data from a different elementary stream of the same type.

The first byte of the payload of the next Transport Stream packettransport packet shall be the first byte of an access point of the elementary stream contained in Transport Stream packettransport packets with that PID value. Thus the previous access unit aligns with the packet boundary or is "stuffed" to make this so. Subsequent to the splicing point, the countdown field may also be present. When the splice_countdown is a negative number whose value is minus n (-n)  it indicates that the associated Transport Stream packettransport packet is the nth packet following the splicing point.

transport_private_data_length -- The transport_private_data_length is an 8 bit field specifying the number of private_data bytes immediately following the transport  private_data_length field.

adaptation_field_extension_length -- The adaptation_field_extension_length  is an 8 bit field. It indicates the length of the extended adaptation field data following the end of this field.

private_data_byte -- The private_data_byte is an 8 bit field that shall not be specified by ISO/IEC.

stuffing_byte -- This is a fixed 8-bit value equal to '1111 1111' that can be inserted by the encoder.  It is discarded by the decoder.

2.4.3.6 PES packet

2.4.3.6

Table 2-7 -- PES Packet2-7

| Syntax | No. of Bits | Mnemonic |  | PES_packet() { |  |  |  | packet_start_code_prefix | 24 | bslbf |  | stream_id | 8 | uimsbf |  | PES_packet_length | 16 | uimsbf |  | if (stream_id != private_stream_2 && stream_id != padding_stream) { |  |  |  | '10' | 2 | bslbf |  | PES_scrambling_control | 2 | bslbf |  | PES_priority | 1 | bslbf |  | data_alignment_indicator | 1 | bslbf |  | copyright | 1 | bslbf |  | original_or_copy | 1 | bslbf |  | PTS_DTS_flags | 2 | bslbf |  | ESCR_flag | 1 | bslbf |  | ES_rate_flag | 1 | bslbf |  | DSM_trick_mode_flag | 1 | bslbf |  | additional_copy_info_flag | 1 | bslbf |  | PES_CRC_flag | 1 | bslbf |  | PES_extension_flag | 1 | bslbf |  | PES_header_data_length | 8 | uimsbf |  | if (PTS_DTS_flags =='10' ) { |  |  |  | '0010' | 4 | bslbf |  | PTS [32.30] | 3 | bslbf |  | marker_bit | 1 | bslbf |  | PTS [29.15] | 15 | bslbf |  | marker_bit | 1 | bslbf |  | PTS [14..0] | 15 | bslbf |  | marker_bit | 1 | bslbf |  | } |  |  |  | if (PTS_DTS_flags ==‘11’ ) { |  |  |  | '0011' | 4 | bslbf |  | PTS [32..30] | 3 | bslbf |  | marker_bit | 1 | bslbf |  | PTS [29..15] | 15 | bslbf |  | marker_bit | 1 | bslbf |  | PTS [14..0] | 15 | bslbf |  | marker_bit | 1 | bslbf |  | '0001' | 4 | bslbf |  | DTS [32..30] | 3 | bslbf |  | marker_bit | 1 | bslbf |  | DTS [29..15] | 15 | bslbf |  | marker_bit | 1 | bslbf |  | DTS [14..0] | 15 | bslbf |  | marker_bit | 1 | bslbf |  | } |  |  |  | if(ESCR_flag=='1'){ |  |  |  | reserved | 2 | bslbf |  | ESCR_base[32..30] | 3 | bslbf |  | marker_bit | 1 | bslbf |  | ESCR_base[29..15] | 15 | bslbf |  | marker_bit | 1 | bslbf |  | ESCR_base[14..0] | 15 | bslbf |  | marker_bit | 1 | bslbf |  | ESCR_extension | 9 | uimsbf |  | marker_bitmarker bit | 1 | bslbf |  | } |  |  |  | if (ES_rate_flag == '1') { |  |  |  | marker_bitmarker bit | 1 | bslbf |  | ES_rate | 22 | uimsbf |  | marker_bitmarker bit | 1 | bslbf |  | } |  |  |  | if(DSM_trick_mode_flag == '1') { |  |  |  | trick_mode_control | 3 | uimsbf |  | if ( trick_mode_control == '000' ) { |  |  |  | field_id | 2 | bslbf |  | intra_slice_refresh | 1 | bslbf |  | frequency_truncation | 2 | bslbf |  | } |  |  |  | else if( trick_mode_control == '001' ){ |  |  |  | field_rep_cntrl | 5 | uimsbf |  | } |  |  |  | else if( trick_mode_control == '010' ) { |  |  |  | field_id | 2 | uimsbf |  | reserved | 3 | bslbf |  | } |  |  |  | else if ( trick_mode_control == '011' ) { |  |  |  | field_id | 2 | bslbf |  | intra_slice_refresh | 1 | bslbf |  | frequency_truncation | 2 | bslbf |  | } |  |  |  | } |  |  |  | if ( additional_copy_info_flag == '1') { |  |  |  | marker_bit | 1 | bslbf |  | additional_copy_info | 7 | bslbf |  | } |  |  |  | if (PES_CRC_flag == '1') { |  |  |  | previous_PES_packet_CRC | 16 | bslbf |  | } |  |  |  | if (PES_extension_flag == '1') { |  |  |  | PES_private_data_flag | 1 | bslbf |  | pack_header_field_flag | 1 | bslbf |  | program_packet_sequence_counter_flag | 1 | bslbf |  | P-STD_buffer_flag | 1 | bslbf |  | reserved | 3 | bslbf |  | PES_extension_field_flag | 1 | bslbf |  | } |  |  |  | if (PES_private_data_flag == '1' ) { |  |  |  | PES_private_data | 128 | bslbf |  | } |  |  |  | if (pack_header_field_flag == '1' ) { |  |  |  | pack_field_length | 8 | uimsbf |  | pack_header() |  |  |  | } |  |  |  | if(program_packet_sequence_counter_flag== '1'){ |  |  |  | marker_bit | 1 | bslbf |  | program_packet_sequence_counter | 7 | uimsbf |  | marker_bit | 1 | bslbf |  | original_stuff_length | 7 | uimsbf |  | } |  |  |  | if ( P-STD_buffer_flag == '1' ) { |  |  |  | '01' | 2 | bslbf |  | P-STD_buffer_scale | 1 | bslbf |  | P-STD_buffer_size | 13 | uimsbf |  | } |  |  |  | if ( PES_extension_field_flag == '1'){ |  |  |  | marker_bit | 1 | bslbf |  | PES_extension_field_length | 7 | uimsbf |  | for(i=0;i<PES_extension_field_length;i++) { |  |  |  | reserved | 8 | bslbf |  | } |  |  |  | } |  |  |  | for (i=0;i<N;i++) { |  |  |  | stuffing_byte | 8 | bslbf |  | } |  |  |  | for (i=0;i<N;i++) { |  |  |  | PES_packet_data_byte | 8 | bslbf |  | } |  |  |  | } |  |  |  | else if (stream_id == private_stream_2) { |  |  |  | for ( i=0;i<PES_packet_length;i++) { |  |  |  | PES_packet_data_byte | 8 | bslbf |  | } |  |  |  | } |  |  |  | else if ( stream_id == padding_stream) { |  |  |  | for ( i=0;i<N;i++) { |  |  |  | padding_byte | 8 | bslbf |  | } |  |  |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.3.7 Semantic definition of fields in PES packet

2.4.3.7

packet_start_code_prefix -- The packet_start_code_prefix is a 24-bit code. Together with the stream_id that follows it constitutes a packet start code that identifies the beginning of a packet.  The packet_start_code_prefix  is the bit string '0000 0000 0000 0000 0000 0001' (0x000001).

stream_id -- The stream_id specifies the type and number of the elementary stream as defined by the stream_id table 2-24 on page 49 .

PES_packet_length -- A 16 bit field specifying the number of bytes in the PES packet following the last byte of the field. A value of 0 indicates that the PES packet length is neither specified nor bounded and is allowed only in PES packets whose payload is a video elementary stream contained  in Transport Stream packettransport packets.

PES_scrambling_control --  The 2 bit PES_scrambling_control indicates the scrambling mode of the PES packet payload.

Table 2-8 -- PES scrambling control values2-8

| Value | Description |  | 00 | NOT scrambled |  | 01 | user defined |  | 10 | user defined |  | 11 | user defined |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

PES_priority -- is a 1 bit field indicating the priority of the payload in this PES packet. A '1' indicates a higher priority of the payload of the PES packet payload than a PES packet payload with this field set to '0'. A multiplexor can use the PES_priority bit to prioritize its data within an elementary stream. This field shall not be changed by the transport mechanism. A value of zero shall not coded when the PES priority is carried in a Program Stream.

data_alignment_indicator -- A 1 bit flag, when set to '1' indicates that the PES packet header is immediately followed by the access unit data type as defined in the data_stream_alignment_descriptor in table 2-42 on page 62. When set to a value of '0' it is not defined whether any such alignment occurs or not.

copyright -- If this bit is set to '1',  it indicates that the contents of the associated PES packet payload is copyrighted. When set to a value of '0' this indicates that the material is not copyrighted.

original_or_copy -- If this bit is set to '1', the contents of the associated PES packet payload is an original. When set to '0' it indicates that it is a copy.

PTS_DTS_flags -- A 2 bit flag. If the PTS_DTS_flags field equals '10', a PTS field is present in the PES packet header. If the PTS_DTS_flags field equals '11', both a PTS and DTS field are present in the PES packet header. If the PTS_DTS_flags field equals '00' neither a PTS nor a DTS field is present in the PES packet header. The value '01' is forbidden.

ESCR_flag -- A 1 bit flag, when set to '1' indicates that an ESCR field is present in the PES packet header.  When set to a value of '0' it indicates that no ESCR fields are present.

ES_rate_flag -- A 1 bit flag when set to '1' indicates that the ES_rate field is present in the PES packet header. When set to a value of '0' it inidcates that no ES_rate field is present.

DSM_trick_mode_flag -- a 1 bit field when set to '1' it indicates the presence of an 8 bit field used for trick_mode_control field. When set to a value of  '0' it indicates that this field is not present.

additional_copy_info_flag -- A 1 bit flag when set to '1' indicates the presence of the additional_copy_info field. When set to a value of  '0' it indicates that this field is not present.

PES_CRC_flag --  A 1 bit flag when set to '1' indicates that a CRC field is present in the PES packet. When set to a value of  '0' it indicates that this field is not present.

PES_extension_flag -- A 1 bit flag, when set to '1' indicates that an extension field of flags exists in this PES packet header. When set to a value of  '0' it indicates that this field is not present.

PES_header_data_length -- An 8 bit field specifying the total number of bytes occupied by the optional fields and any stuffing bytes contained in this PES packet header. The presence of optional fields is indicated in the byte that precedes the PES_header_data_length field.

marker_bit -- A marker_bit is a 1 bit field that has the value '1'.

PTS (presentation_time_stamp) -- The PTS  is a 33-bit number coded in three separate fields. It indicates the intended time of presentation in the system target decoder of the presentation unit that corresponds to the first access unit that commences in the packet. The value of PTS is measured in the number of periods of a 90kHz system clock with a tolerance specified in clause 2.4.2 on page 11.  Using the notation of clause 2.4.2 on page 11 the value encoded in the presentation_time_stamp is:

(2-8)
2-8

where

tpn(k) is the presentation time of presentation unit Pn(k).

Pn(k) is the presentation unit corresponding to the first access unit that commences in the packet data.    An access unit commences in the packet if the first byte of the access unit is contained in the packet data. (see 2.4.1 for a definition of the first byte of audio and video access units).

If there is filtering in audio, it is assumed by the system model that filtering introduces no delay, hence the sample referred to by PTS at encoding is the same sample referred to by PTS at decoding. Refer to clause 2.5.7.5.

DTS (decoding_time_stamp) -- The DTS is a 33-bit number coded in three separate fields. It indicates the intended time of decoding in the system target decoder of the first access unit that commences in the packet.  The value of DTS is measured in the number of periods of a 90kHz system clock with a tolerance specified in clause 2.4.2 on page 11.  Using the notation of clause 2.4.2 on page 11 the value encoded in the decoding_time_stamp is:

(2-9)
2-9

where

tdn(j) is the decoding time of access unit An(j).

An(j) is the first access unit that commences in the packet data. An access unit commences in the packet if the first byte of the access unit is contained in the packet data. (see 2.4.1 for a definition of the first byte of audio and video access units).

Refer to clause 2.5.7.6

ESCR -- The elementary_stream_clock_reference (ESCR) is an optional 42 bit field coded as a 33 bit base field (ESCR_base) with a 9 bit extension field (ESCR_ext). It indicates the intended time of arrival of the byte containing the last bit of the ESCR_base at the input of the system target decoder when present in a PES Stream. The value of the ESCR_base is measured in the number of periods of a 90kHz system clock with a tolerance specified in clause 2.4.2 on page 11.

Specifically:

(2-10)
2-10

(2-11)
2-11

(2-12)
2-12

The ESCR_extension field indicates the number of periods of a 27MHz clock after a 90kHz period start. The value of this field will be between 0 and 299. When the value equals 299, the ESCR_ext will wrap around to 0 and simultaneously the ESCR_base field will increment by 1. Refer to clause 2.5.7.4.

ES_rate -- The elementary_stream_rate (ES_rate) field is a positive integer specifying the rate at which the system target decoder receives bytes of the PES packet in the case of a PES stream. The ES_rate is valid in the PES packet in which it is included and in subsequent PES packets of the same PES stream until a new ES_rate field is encountered. The value of the ES_rate is measured in units of 50 bytes/second rounded upwards. The value 0 is forbidden. The value of the ES_rate is used to define the time of arrival of bytes at the input of a P-STD for PES streams in clause 2.5.2 on page 41 of this Recommendation | International Standard. The value encoded in the ES_rate field may vary from PES_packet to PES_packet.

trick_mode_control -- A three (3) bit field used to indicate the mode in which the DSM operates. The values for each mode is in the table below.

Table 2-9 -- Trick mode control values2-9

| value | description |  | '000' | fast forward |  | '001' | slow motion |  | '010' | freeze frame |  | '011' | fast reverse |  | '1xx' | reserved |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

fast forward-When the value '000' is coded, then the DSM is in the fast forward mode. The DSM will ensure that the buffers in the STD model do not overflow. The DSM will provide each picture with valid timestamps. During the fast forward mode, the system time clock in the STD model is continuous. However, at the transition to another mode, a discontinuity in the system time clock will occur. When intra_slice_refresh bit is set in the video elementary stream ( see Part 2 of this Recommendation | International Standard), it indicates that each picture is composed of intra slices with possible gaps between them. The decoder may replace the missing slices by repeating the co-sited slices of previously decoded picture(s). The field_id flag is to be interpreted in the same ways as for the freeze frame mode.

The field "frequency_truncation" provides an indication of coefficient selection done by the DSM in the process of generating the bitstream in fast play modes.

Table 2-10 -- Coefficient selection values2-10

| Value | Description |  | '00' | Only DC coefficients are sent |  | '01' | the first three coefficients in scan order on average |  | '10' | the first six coefficients in scan order on average |  | '11' | all coefficients may be sent |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

slow motion-If the value of '001' is encoded, then the DSM is in slow motion mode. The DSM will provide a picture with valid time stamps to the decoder. In the slow motion mode, the PTS indicates the value of the system time clock at which the first field from the associated picture is to be displayed in the STD model. During the slow motion mode, the system time clock in the STD model is continuous. However, at the transition to another mode, a discontinuity in the system time clock will occur. The field_rep_cntrl value is used to indicate to the decoder how many field times it needs to repeat the display of field #1 of the received picture as both top and bottom fields alternatingly. The same value also indicates to the decoder how often field #2 has to be repeated after the repetition of field #1 has been completed.  For progressive pictures the decoder interprets the value specified by field_rep_cntrl field in terms of complete frames. The DSM will then provide the next picture to the decoder with the correct presentation time stamp (i.e. taking into account how many times the fields of the previous picture were repeated) along with the appropriate value of the field_rep_cntrl field. If the value of field_rep_cntrl is 0, this is be interpreted in the same way as freeze frame, field_id = ' 10'. The field_rep_cntrl field shall not be coded with a value indicating a number of field repetitions less than in the case of playback at normal speed.

freeze frame-If the value '010' is encoded, then the DSM is in freeze frame mode. In the freeze frame mode, the PTS indicates the value of the system time clock at which the first field from the associated picture to be frozen is to be displayed in the STD model. During the freeze frame mode, the system time clock in the STD model is continuous. However, at the transition to another mode, a discontinuity in the system time clock will occur. The DSM will provide a picture with valid time stamps to the decoder. The field_id flag is only meaningful when dealing with interlaced pictures. In this case these bits are to be interpreted as follows:

Table 2-11 -- Freeze frame control values2-11

| value | description |  | '00' | display from field 1 only |  | '01' | display from field 2 only |  | '10' | display complete frame |  | '11' | reserved |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

In this definition, displaying from a single field implies repeating the specified field as top and bottom fields alternately until another mode is specified. The DSM temporarily stops providing additional data to the decoder. The decoder buffer may under-flow in this mode.

fast reverse-When the value '011' is encoded, then the DSM is in the fast reverse mode. The DSM will ensure that the buffers in the STD model do not overflow. The DSM will provide each picture with valid timestamps. During the fast reverse mode, the system time clock in the STD model is continuous. However, at the transition to another mode, a discontinuity in the system time clock will occur. When intra_slice_refresh bit is set, it indicates that each picture is composed of intra slices with possible gaps between them. The decoder may replace the missing slices by repeating the co-sited slices of previously decoded picture(s). The field_id flag is to be interpreted in the same ways as for the freeze frame mode. The "frequency_truncation" field provides an indication of coefficient selection done by the DSM in the process of generating the bitstream in fast play modes.

Table 2-12 -- Fast reverse control values2-12

| Value | Description |  | '00' | Only DC coefficients are sent |  | '01' | the first three coefficients in scan order on average |  | '10' | the first six coefficients in scan order on average |  | '11' | all coefficients may be sent |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

additional_copy_info: This field contains private data relating to copyright information.

previous_PES_packet_CRC -- The previous_PES_packet_CRC is a 16 bit polynomial given by the equation:

X16+X12+X5+1

The message data to be error checked is processed with the check polynomial by dividing the message data by previous_PES_packet_CRC. This field is calculated over the PES packet data bytes in the previous PES packet being transported in the same PID. The initial vector for the CRC computation shall be 0xFFFF. The resulting 16 bit remainder is placed directly into the previous_PES_packet_CRC field.

Note- This CRC is intended for use in network maintenance such as isolating the source of intermittent errors. It is not intended for use by elementary steam decoders. It is calculated only over the data bytes because PES packet header data can be modified during transport.

PES_private_data_flag -- is a 1 bit flag, when set to  '1' indicates that the PES packet header contains private data. When set to a value of  '0' it indicates that private data is not present in the PES header.

pack_header_field_flag -- A 1 bit flag when set to '1' indicates that an ISO/IEC 11172 pack header or an ISO/IEC 13818 Program Stream pack header is stored in this PES packet header. If this field is in a PES packet that is contained in a Program Stream, then this field shall be set to '0'. In a Transport Stream when set to a value '0' it indicates that no pack header is present in the PES header.

program_packet_sequence_counter_flag -- A 1 bit flag, when set to '1' indicates that the program_sequence_counter and original_stuff_length fields are present in this PES packet. When set to a value of '0' it indiates that these fields are not present in the PES header.

P-STD_buffer_flag -- A 1 bit flag, when set to  '1' indicates that the P-STD_buffer_scale and P-STD_buffer_size are available in the PES packet header. When set to a value of '0' it indiates that these fields are not present in the PES header.

PES_extension_field_flag -- This is a 1 bit field, when set to '1' indicates the presence of the PES_extension_field.

PES_private_data -- This is a 16 byte field which contains private data. This data, combined with the fields before and after, shall not emulate the packet_start_code_prefix. (0x000001).

pack_field_length -- This is a 8 bit field which indicates the length, in bytes, of the pack_header_field().

program_packet_sequence_counter -- The program_packet_sequence_counter field is an 87 bit field. It is an optional counter that increments with each successive PES packet in the program multiplex. This allows an application to retrieve the original PES packet sequence of an ISO/IEC 13818 Program Stream. The counter will wrap around to 0 after its maximum value. Repetition of PES packets shall not occur. Consequently, no two consecutive PES packets in the program multiplex shall have identical program_packet_sequence_counter values.

original_stuff_length -- This 7 bit field specifies the number of stuffing bytes used in the ISO/IEC 11172 packet header.

stuffing_byte -- This is a fixed 8-bit value equal to '1111 1111' that can be inserted by the encoder for example to meet the requirements of the digital storage medium.  It is discarded by the decoder.  No more than 32 stuffing bytes shall be present in 1 PES packet header.

P-STD_buffer_scale[Program Stream only] -- The P-STD_buffer_scale is a 1 bit field that indicates the scaling factor used to interpret the subsequent P-STD_buffer_size field.  If the preceding stream_id indicates an audio stream, P-STD_buffer_scale shall have the value '0'.  If the preceding stream_id indicates a video stream, P-STD_buffer_scale shall have the value '1'.  For all other stream types, the value may be either '1' or '0'.

P-STD_buffer_size[Program Stream only] --The P-STD_buffer_size is a 13-bit unsigned integer defining the size of the input buffer, BSn, in the P-STD.  If  P-STD_buffer_scale has the value '0' then the P-STD_buffer_size measures the buffer size in units of 128 bytes.  If  P-STD_buffer_scale has the value '1' then the P-STD_buffer_size measures the buffer size in units of 1024 bytes.  Thus:

if (P-STD_buffer_scale == 0)

BSn = P-STD_buffer_size  128;	(2-13)
2-13

else

BSn = P-STD_buffer_size  1024;	(2-14)
2-14

The encoded value of the P-STD buffer size takes effect immediately when the P-STD_buffer_size field is received by the ISO/IEC 13818 System Target Decoder. Refer to 2.4.9.7.

PES_extension_field_length -- This 7 bit field specifies the length, in bytes, of the data following this field in the PES_extension_field.

PES_packet_data_byte -- PES_packet_data_bytes shall be contiguous bytes of data from the elementary stream indicated by the packet's stream_id or PID.  The byte-order of the elementary stream shall be preserved. The number of PES packet_data_bytes, N, is specified by the PES_packet_length field. N shall be equal to the value indicated in the PES_packet_length minus the number of bytes between the last byte of the PES_packet_length field and the first PES_packet_data_byte.

In the case of a private_stream_1 or private_stream_2, the contents of the PES_packet_data_byte field is user definable and will not be specified by ISO in the future.

padding_byte -- This is a fixed 8 bit value equal to '1111 1111' that can be inserted by the encoder, for example, to meet the requirements of the DSM. It is discarded by the decoder.

2.4.4	Program specific information

2.4.4

Program Specific Information (PSI) includes both ISO/IEC 13818 normative data and private data that enable de-multiplexing of programs by decoders. Programs are composed of one or more elementary streams, each labeled with a PID. Programs or elementary streams or parts thereof may be conditionally accessed. However, Program Specific Information shall not be scrambled.

In Transport Streams Program Specific Information (PSI) is classified into four table structures as shown in the table below. While these structures may be thought of as simple tables, they shall be segmented into sections and inserted in ISO/IEC 13818 Transport Stream packets.

Table 2-13 -- Program specific information2-13

| Structure Name | Stream Type | Reserved PID # | Description |  | Program Association Table | ISO/IEC 13818 | 0x00 | Associates Program Number and Program Map Table PID |  | Program Map Table | ISO/IEC 13818 | Assigned | Specifies PID values for components of one or more programs |  | Network Information Table | Private | Assigned | Physical network parameters such as FDM frequencies, Transponder Numbers, etc. |  | Conditional Access Table | ISO/IEC 13818 | 0x01 | Associates one or more (private) EMM streams each with a unique PID value |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

ISO/IEC 13818-defined PSI tables shall be segmented into one or more sections that are carried within transports packets. A section is a syntactic structure that shall be used for mapping all ISO/IEC 13818-defined PSI tables into Transport Stream packettransport packets.

Along with ISO/IEC 13818-defined PSI tables, it is possible to carry private data tables. The means by which private information is carried within Transport Stream packettransport packets shall be private. It may be structured in the same manner used for carrying of ISO/IEC 13818-defined PSI tables, such that the syntax for mapping this private data is identical to that used for the mapping of ISO/IEC 13818-defined PSI tables. For this purpose, a private section is defined. If the private data is carried in Transport Stream packettransport packets with the same PID value as Transport Stream packettransport packets carrying Program Map Tables, (as identified in the Program Association Table), then the private_section syntax and semantics shall be used. This private_section allows data to be transmitted with a minimum of structure. When this structure is not used, the mapping of private data within Transport Stream packettransport packets is not defined by ISO/IEC 13818.

Sections may be variable in length.. The beginning of a section is indicated by a pointer_field in the Transport Stream packettransport packet payload. The syntax of this field is specified in table Error! Reference source not found. on page 31.

Within a Transport Stream packet stuffing bytes of value 0xFF may be found after the last byte of a section, in which case all following bytes until the end of the Transport Stream packet shall also be stuffing bytes of value 0xFF. These byte may be discarded by a decoder. In such a case, the payload of the next Transport Stream packet with the same PID value shall begin with a pointer_field of value 0x00 indicating that the next section starts immediately thereafter.

All Transport Streams shall contain one or more Transport Stream packets with PID value 0x0000. These Trnsport Stream packets together shall contain a complete list of all programs within the Transport Stream. The most recently transmitted version of the table with the current_next_indicator set to a value of  '1' shall always apply to the current data in the Transport Stream. Any changes in the programs carried within the Transport Stream shall be described in an updated version of the Program Association Table carried in Transport Stream packets with PID value 0x0000. These sections shall all use table_id value 0x00. Only sections with this value of table_id are permitted within Transport Stream packets with PID value of 0x0000.

Whenever one or more elementary streams within a Transport Stream are scrambled, Transport Stream packets with a PID value 0x0001 shall be transmitted containing CA_sections containing CA_descriptors appropriate to the scrambled streams. The transmitted Transport Stream packets shall together form one complete version of the conditional access table. The most recently transmitted version of the table with the current_next_indicator set to a value of '1' shall always apply to the current data in the Transport Stream. Any changes in scrambling making the existing table invalid or incomplete shall be described in an updated version of the conditional access table. These sections shall all use table_id value 0x01. Only sections with this table_id value are permitted within Transport Stream packets with a PID value of 0x0001.

All Transport Streams shall contain one or more Transport Stream packets with PID values which are labled under the program association table as Transport Stream packets containing TS program map sections. Every program listed in the program association table shall be described in a single TS program map section. Every program shall be fully described within the Transport Stream itself. The most recently transmitted version of the TS_program_map_section with the current_next_indicator set to a value of '1' shall always apply to the current data within the Transport Stream. Any changes in the definition of any of the programs carried within the Transport Stream shall be described in an updated version of the corresponding section of the program map table carried in Transport Stream packets with the PID value identified as the PMT_PID for that specific program.  All Transport Stream packets which carry a given Program Map section shall have the same PID value.

Sections with a table_id value of 0x02 shall contain program map table information. Such sections may be carried in Transport Stream packets with different PID values.

The Network Information Table is optional and its contents are private. If present it is carried within Transport Stream packettransport packets that shall have the same PID value, called the network_PID. The network_PID value is defined by the user and, when present, shall be found in the Program Association Table under the reserved program_number 0x0000. If the network information table exists it shall take the form of one or more private_sections.

The maximum number of bytes in a section of a ISO/IEC 13818-defined PSI table is 1K(1024 bytes). The maximum number of bytes in a private_section is 4K (4096 bytes).

There are no restrictions on the occurrence of start codes, sync bytes or other bit patterns in PSI data, whether ISO/IEC 13818 or private.

2.4.4.1 Pointer

The pointer_field syntax is defined in table 2-14 below.2.4.4.1

Table 2-14 -- Program specific information pointer

| syntax | No. of bits | Mnemonic |  | pointer_field | 8 | uimsbf |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

2.4.4.2 Semantics definition of fields in pointer syntax

2.4.4.2

pointer_field -- This is an 8-bit field whose value shall be the number of bytes, immediately following  the pointer_field until the first byte of the first section that is present in the payload of the Transport Stream packettransport packet (so a value of 0x00 in the pointer_field indicates that the section starts immediately after the pointer_field). When at least one section begins in a given Transport Stream packettransport packet, then the payload_unit_start_indicator shall be set to 1 and the first byte of  the payload of that Transport Stream packettransport packet shall contain the pointer. When no section begins in a given Transport Stream packettransport packet, then the payload_unit_start_indicator shall be set to 0 and no pointer shall be sent in the payload of that packet.

2.4.4.3 Stream types

2.4.4.3

The stream types specified in table 2-31 are valid for both Transport Stream and Program Stream Program Specific Information.

2.4.4.4 Specification of the program association table

2.4.4.4

The Program Association Table provides the correspondence between a program_number and the PID value of the Transport Stream packettransport packets which carry the program definition. The program_number is the numeric label associated with a program.

Program number 0x0000 is reserved to specify the network PID.  This identifies the Transport Stream packettransport packets which carry the Network Information Table.

The overall table is to be split into one or more sections with the following syntax.

2.4.4.5 Program association table

2.4.4.5

Table 2-15 -- Program association section2-15

| Syntax | No. of bits | Mnemonic |  | program_association_section() { |  |  |  | table_id | 8 | uimsbf |  | section_syntax_indicator | 1 | bslbf |  | '0' | 1 | bslbf |  | reserved | 2 | bslbf |  | section_length | 12 | uimsbf |  | transport_stream_id | 16 | uimsbf |  | reserved | 2 | bslbf |  | version_number | 5 | uimsbf |  | current_next_indicator | 1 | bslbf |  | section_number | 8 | uimsbf |  | last_section_number | 8 | uimsbf |  | for (i=0; i<N;i++) { |  |  |  | program_number | 16 | uimsbf |  | reserved | 3 | bslbf |  | if(program_number == '0') { |  |  |  | network_PID | 13 | uimsbf |  | } |  |  |  | else { |  |  |  | program_map_PID | 13 | uimsbf |  | } |  |  |  | } |  |  |  | CRC_32 | 32 | rpchof |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.4.6 Table_id assignments

The table_id field identifies the content of a Transport Stream PSI section as shown in table 2-16 below.

Table 2-16 -- table_id assignment values2-16

| value | description |  | 0x00 | program_association_section |  | 0x01 | conditional access_section |  | 0x02 | program_map_section |  | 0x03-0x3F | ISO/IEC 13818 reserved |  | 0x40-0xFE | User private |  | 0xFF | forbidden |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.4.7 Sematics for fields in program association section

2.4.4.7

table_id -- This is an 8 bit field, which shall be set to 0x00 as shown in table 2-16 above.

section_syntax_indicator -- The section_syntax_indicator is a 1 bit field which shall be set to '1'.

section_length -- This is a twelve bit field, the first two bits of which shall be '00'. It specifies the number of bytes of the section, starting immediately following the section_length field, and including the CRC.

transport_stream_id -- This is a 16 bit field which serves as a label to identify this Transport Stream from any other multiplex within a network. Its value is defined by the user.

version_number -- This 5 bit field is the version number of the whole Program Association Table. The version number shall be incremented by 1 whenever the definition of the Program Association Table changes. Upon reaching the value 31, it wraps around to 0. When the current_next_indicator is set to '1', then the version_number shall be that of the currently applicable Program Association Table. When the current_next_indicator is set to '0', then the version_number shall be that of the next applicable Program Association Table.

current_next_indicator -- A 1 bit indicator, which when set to '1' indicates that the Program Association Table sent is currently applicable. When the bit is set to '0', it indicates that the table sent is not yet applicable and shall be the next table to become valid.

section_number -- This 8 bit field gives the number of this section. The section_number of the first section in the Program Association Table shall be 0x00. It shall be incremented by 1 with each additional section in the Program Association Table.

last_section_number -- This 8 bit field specifies the number of the last section (that is, the section with the highest section_number) of the complete Program Association Table.

program_number -- Program_number is a 16 bit field. It specifies the program to which the program_map_PID is applicable. If this is set to 0x0000 then the following PID reference shall be the network PID. For all other case the value of this field is user defined. This field shall not take any single value more than once within one version of the program association table.

network_PID -- Network_PID is a 13 bit field specifying the PID of the Transport Stream packettransport packets which shall contain the Network Information Table. The value of the network_PID field is defined by the user but shall not take values reserved for other purposes. The presence of the network_PID is optional.

program_map_PID -- program_map_PID is a 13 bit field specifying the PID of the Transport Stream packettransport packets which shall contain the program_map_section applicable for the program as specified by the program_number. No program_number shall have more than one program_map_PID assignment. The value of the program_map_PID is defined by the user, but shall not take the values reserved for other purposes.

CRC_32 -- CRC_32 is a 32 bit polynomial given by the equation:

x32+x26+x23+x22+x16+x12+x11+x10+x8+x7+x5+x4+x2+x+1.

The message data to be error checked is processed with the check polynomial by dividing the message data by CRC_32. The initial vector for the CRC computation shall be 0xFFFFFFFF. The resulting 32 bit remainder is placed directly into the CRC_32 field.

2.4.4.8 Conditional access table

2.4.4.8

The Conditional Access (CA) Table provides the association between one or more CA systems, their EMM streams and any special parameters associated with them.

The table may be segmented into one or more sections, before insertion into Transport Stream packettransport packets, with the following syntax .

Table 2-17 -- Conditional access section2-17

| Syntax | No. of bits | Mnemonic |  | CA_section() { |  |  |  | table_id | 8 | uimsbf |  | section_syntax_indicator | 1 | bslbf |  | '0' | 1 | bslbf |  | reserved | 2 | bslbf |  | section_length | 12 | uimsbf |  | reserved | 18 | bslbf |  | version_number | 5 | uimsbf |  | current_next_indicator | 1 | bslbf |  | section_number | 8 | uimsbf |  | last_section_number | 8 | uimsbf |  | for (i=0; i<N;i++) { |  |  |  | descriptor() |  |  |  | } |  |  |  | CRC_32 | 32 | rpchof |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.4.9 Semantic definition of fields in conditional access section

2.4.4.9

table_id -- This is an 8 bit field, which shall be always set to 0x01 as shown in table 2-16 above.

section_syntax_indicator -- The section_syntax_indicator is a 1 bit field which shall be set to '1'.

section_length -- This is a twelve bit field, the first two bits of which shall be '00'. It specifies the number of bytes of the section starting immediately following the section_length field, and including the CRC.

version_number -- This 5 bit field is the version number of the whole conditional access table. The version number shall be incremented by 1 when a change in the information carried within the CA table occurs. When it reaches the value 31, it wraps around to 0. When the current_next_indicator is set to '1', then the version_number shall be that of the currently applicable Conditional Access Table. When the current_next_indicator is set to '0', then the version_number shall be that of the next applicable Conditional Access Table.

current_next_indicator -- A 1 bit indicator, which when set to '1' indicates that the Conditional Access Table sent is currently applicable. When the bit is set to '0', it indicates that the Conditional Access Table sent is not yet applicable and shall be the next Conditional Access Table to become valid.

section_number -- This 8 bit field gives the number of this section. The section_number of the first section in the Conditional Access Table shall be 0x00. It shall be incremented by 1 with each additional section in the Conditional Access Table.

last_section_number -- This 8 bit field specifies the number of the last section (that is, the section with the highest section_number) of the Conditional Access Table.

CRC_32 -- CRC_32 is a 32 bit polynomial given by the equation:

x32+x26+x23+x22+x16+x12+x11+x10+x8+x7+x5+x4+x2+x+1.

The message data to be error checked is processed with the check polynomial by dividing the message data by CRC_32. The initial vector for the CRC computation shall be 0xFFFFFFFF. The resulting 32 bit remainder is placed directly into the CRC_32 field.

2.4.4.10 Program Map Table

2.4.4.10

The Program Map Table provides the mappings between program numbers and the elementary streams that comprise them.  A single instance of such a mapping is referred to as a "program definition". The program map table is the complete collection of all program definitions for a Transport Stream. This table shall be transmitted in packets, the PID values of which are privately selected. More than one PID value may be used, if desired. The table may be segmented into one or more sections, before insertion into Transport Stream packettransport packets, with the following syntax .

Table 2-18 -- Transport Stream program map section2-18

| Syntax | No. of bits | Mnemonic |  | TS_program_map_section() { |  |  |  | table_id | 8 | uimsbf |  | section_syntax_indicator | 1 | bslbf |  | '0' | 1 | bslbf |  | reserved | 2 | bslbf |  | section_length | 12 | uimsbf |  | program_number | 16 | uimsbf |  | reserved | 2 | bslbf |  | version_number | 5 | uimsbf |  | current_next_indicator | 1 | bslbf |  | section_number | 8 | uimsbf |  | last_section_number | 8 | uimsbf |  | reserved | 3 | bslbf |  | PCR_PID | 13 | uimsbf |  | reserved | 4 | bslbf |  | program_info_length | 12 | uimsbf |  | for (i=0; i<N; i++) { |  |  |  | descriptor() |  |  |  | } |  |  |  | for (i=0;i<P;i++) { |  |  |  | stream_type | 8 | uimsbf |  | reserved | 3 | bslbf |  | elementary_PID | 13 | uimsnf |  | reserved | 4 | bslbf |  | ES_info_length | 12 | uimsbf |  | for (i=0; i<Q; i++) { |  |  |  | descriptor() |  |  |  | } |  |  |  | } |  |  |  | CRC_32 | 32 | rpchof |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.4.11 Semantics definition of fields in Transport Stream program map section

2.4.4.11

table_id -- This is an 8 bit field, which in the case of a TS_program_map_section shall be always set to 0x02.

section_syntax_indicator -- The section_syntax_indicator is a 1 bit field which shall be set to '1'.

section_length -- This is a twelve bit field, the first two bits of which shall be '00'. It specifies the number of bytes of the section starting immediately following the section_length field, and including the CRC.

program_number -- Program_number is a 16 bit field. It specifies the program to which the program_map_PID is applicable. One program definition shall be carried within only one TS_program_map_section. This implies that a program definition is never longer than 1016 bytes. See Informative Annex  C for ways to deal with the cases when that length is not sufficient.

version_number -- This 5 bit field is the version number of the TS_program_map_section. The version number shall be incremented by 1 when a change in the information carried within the section occurs. Upon reaching the value 31, it wraps around to 0. Version number refers to the definition of a single program, and therefore to a single section. When the current_next_indicator is set to '1', then the version_number shall be that of the currently applicable TS_program_map_section. When the current_next_indicator is set to '0', then the version_number shall be that of the next applicable TS_program_map_section.

current_next_indicator -- A 1 bit indicator, which when set to '1' indicates that the TS_program_map_section sent is currently applicable. When the bit is set to '0', it indicates that the TS_program_map_section sent is not yet applicable and shall be the next TS_program_map_section to become valid.

section_number -- The value of this 8 bit field shall be always 0x00.

last_section_number -- The value of this 8 bit field shall be always 0x00.

PCR_PID -- This is a 13 bit field indicating the PID of the Transport Stream packettransport packet which shall contain the PCR  fields valid for the program specified by program_number.If no PCR is associated with a program definition for private streams then this field shall take the value of 0x1FFF.

program_info_length -- This is a twelve bit field, the first two bits of which shall be '00'. It specifies the number of bytes of  the descriptors immediately following the program_info_length field.

stream_type -- This is an 8 bit field specifying the type of elementary stream or payload carried within the packets with the PID whose value is specified by the elementary_PID. The values of stream_type are specified in table 2-26 on page 52.

elementary_PID -- This is a 13 bit field specifying the PID of the Transport Stream packets which carry the associated elementary stream or payload.

ES_info_length -- This is a twelve bit field, the first two bits of which shall be '00'. It specifies the number of bytes of the descriptors of the associated elementary stream immediately following the ES_info_length field.

CRC_32 -- CRC_32 is a 32 bit polynomial given by the equation:

x32+x26+x23+x22+x16+x12+x11+x10+x8+x7+x5+x4+x2+x+1.

The message data to be error checked is processed with the check polynomial by dividing the message data by CRC_32. The initial vector for the CRC computation shall be 0xFFFFFFFF. The resulting 32 bit remainder is placed directly into the CRC_32 field.

2.4.4.12 Syntax of the Private section

2.4.4.12

The use of the private_section is mandatory when private data is sent in Transport Stream packettransport packets with a PID value designated as a Program Map Table PID in the Program Association Table. This private_section allows data to be transmitted with the absolute minimum of structure to enable an ISO/IEC 13818 decoder to parse the stream. The sections may be used in two ways:  if the section_syntax_indicator is set to '1', then the whole structure common to all tables shall be used; if the indicator is set to '0', then only the first four fields shall follow the common structure syntax and semantics and the rest of the private_section may take any form the user determines. Examples of extended use of this syntax are found in Informative Annex C.

A private table may be made of several private_sections, all with the same table_id.

Table 2-19 -- Private section2-19

| Syntax | No. of bits | Mnemonic |  | private_section() { |  |  |  | table_id | 8 | uimsbf |  | section_syntax_indicator | 1 | bslbf |  | private_indicator | 1 | bslbf |  | reserved | 2 | bslbf |  | private_section_length | 12 | uimsbf |  | if ( section_syntax_indicator == '0') { |  |  |  | for ( i=0;i<N;i++) { |  |  |  | private_data_byte | 8 | bslbf |  | } |  |  |  | } |  |  |  | else { |  |  |  | table_id_extension | 16 | uimsbf |  | reserved | 2 | bslbf |  | version_number | 5 | uimsbf |  | current_next_indicator | 1 | bslbf |  | section_number | 8 | uimsbf |  | last_section_number | 8 | uimsbf |  | for ( i=0;i<private_section_length-9;i++) { |  |  |  | private_data_byte | 8 | bslbf |  | } |  |  |  | CRC_32 | 32 | rpchof |  | } |  |  |  | } |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2.4.4.13 Semantic definition of fields in private section

2.4.4.13

table_id -- This an 8-bit field, the value of which identifies the Private Table this section belongs to. Some values are reserved (table 2-16 on page 34).

section_syntax_indicator -- This is a 1 bit indicator. Set to '1', it indicates that the private section header follows the generic section header syntax beyond the private_section_length field. Set to '0', it indicates that the private_data_bytes are immediately following the private_section_length field.

private_indicator -- This is a 1 bit user definable flag that shall not be specified by ISO/IEC in the future

private_section_length -- A 12-bit field. It specifies the number of remaining bytes in the private section immediately following the private_section_length field up to the end of the private_section.

private_data_byte -- The private_data_byte field is user definable and shall not be specified by ISO in the future.

table_id_extension -- This is a 16-bit field. Its use and value are defined by the user.

version_number -- This 5-bit field is the version number of the private_section. The version_number shall be incremented by 1 when a change in the information carried within the private_section occurs. Upon reaching value 31, it wraps around to 0. When the current_next_indicator is set to '0', then the version_number shall be that of the next applicable private_section with the same table_id and section_number.

current_next_indicator -- A 1 bit indicator, which when set to '1' indicates that the private_section sent is the currently applicable section. When the current_next_indicator is set to '1', then the version_number shall be that of the currently applicable private_section. When the bit is set to '0', it indicates that the private_section sent is not yet applicable and shall be the next private_section with the same section_number and table_id to become valid.

section_number -- This 8-bit field gives the number of the private_section. The section_number of the first section in a private table shall be 0x00. The section_number shall be incremented by 1 with each additional section in this private table.

last_section_number -- This 8-bit field specifies the number of the last section (that is, the section with the highest section_number) of the private table of which this section is a part.

CRC_32 -- CRC_32 is a 32 bit polynomial given by the equation:

x32+x26+x23+x22+x16+x12+x11+x10+x8+x7+x5+x4+x2+x+1.

The message data to be error checked is processed with the check polynomial by dividing the message data by CRC_32. The initial vector for the CRC computation shall be 0xFFFFFFFF. The resulting 32 bit remainder is placed directly into the CRC_32 field.

2.5	Program Stream bitstream requirements

2.5

2.5.1	Program Stream coding structure and parameters

2.5.1

The Program Stream coding layer allows one or more elementary streams to be combined into a single stream. Data from each elementary stream is multiplexed and encoded together with information that allows elementary streams to be replayed in synchronism.

An ISO/IEC 13818 Program Stream consists of one or more elementary streams from one program multiplexed together. Each elementary stream consists of access units, which are the coded representation of presentation units.  The presentation unit for a video elementary stream is a picture.  The corresponding access unit includes all the coded data for the picture.  The access unit containing the first coded picture of a group of pictures also includes any preceding data from that group of pictures, as defined in Part 2 of this Recommendation | International Standard starting with the group_start_code.  The Access Unit containing the first coded picture after a sequence header, as defined in Part 2 of this Recommendation | International Standard also includes that sequence header.  The sequence_end_code is included in the Access Unit containing the last coded picture of a sequence.  (See Part 2 for the definition of the sequence_end_code).  The presentation unit for an audio elementary stream is the set of samples that corresponds to samples from an audio frame (see Part 3 of this Recommendation | International Standard for the definition of an audio frame).

Data from elementary streams is stored in PES packets.  A PES packet consists of a PES packet header followed by packet data.

The PES packet header begins with a 32-bit start-code that also identifies the stream (see table 2-24 on page 49) to which the packet data belongs.  The PES packet header may contain decoding and/or presentation time-stamps (DTS and PTS) that refer to the first access unit that commences in the packet. The PES packet header also contains a number of flags opening a range of optional fields. The packet data contains a variable number of contiguous bytes from one elementary stream.

In a Program Stream PES packets are organized in packs.  A pack commences with a pack header and is followed by zero or more PES packets.  The pack header begins with a 32-bit start-code.  The pack header is used to store timing and bitrate information.

The Program Stream begins with a system header that optionally may be repeated.  The system header carries a summary of the system parameters defined in the stream.

This standard does not specify the coded data which may be used as part of conditional access systems. The standard does however provide mechanisms for program service providers to transport and identify this data for decoder processing, and to reference correctly data which are specified by the standard.

2.5.2	Program Stream system target decoder

2.5.2

The semantics of the Program Stream specified in clause 2.5.3 on page 44 and the constraints on these semantics specified in clause 2.5.7 on page 69 require exact definitions of decoding events and the times at which these events occur.  The definitions needed are set out in this Recommendation | International Standard using a hypothetical decoder known as the Program Stream system target decoder (P-STD).

The P-STD is a conceptual model used to define these terms precisely and to model the decoding process during the construction of ISO/IEC 13818 Program Streams. The P-STD is defined only for this purpose.  Neither the architecture of the P-STD nor the timing described precludes uninterrupted, synchronized play-back of ISO/IEC 13818 Program Streams from a variety of decoders with different architectures or timing schedules.

Figure 2-7 -- ISO/IEC 13818 Program Stream system target decoder notation2-7

The following notation is used to describe the Program Stream system target decoder and is partially illustrated in figure 2-7 above.

i, i'	are indices to bytes in the ISO/IEC 13818 Program Stream.  The first byte has index 0.

j	is an index to access units in the elementary streams.

k, k',k''	are indices to presentation units in the elementary streams.

n	is an index to the elementary streams.

M(i)	is the ith byte in the Program Stream.

tm(i)	indicates the time in seconds at which the ith byte of the ISO/IEC 13818 Program Stream enters the system target decoder.  The value tm(0) is an arbitrary constant.

SCR(i)	is the time encoded in the SCR field measured in units of the 27 MHz system clock where i is the byte index of the final byte of the SCR field.

An(j)	is the jth access unit in elementary stream n.  Note that access units are indexed in decoding order.

tdn(j)	is the decoding time, measured in seconds, in the system target decoder of the jth access unit in elementary stream n.

Pn(k)	is the kth presentation unit in elementary stream n.

tpn(k)	is the presentation time, measured in seconds, in the system target decoder of the kth presentation unit in elementary stream n.

t	is time measured in seconds.

Fn(t)	is the fullness, measured in bytes, of the system target decoder input buffer for elementary stream n at time t.

Bn	the input buffer in the system target decoder for elementary stream n.

BSn	is the size of the system target decoder input buffer, measured in bytes, for elementary stream n.

Dn	is the decoder for elementary stream n.

On	is the reorder buffer for video elementary stream n.

System clock frequency

Timing information referenced in P-STD is carried by several data fields defined in this Recommendation | International Standard. The fields are defined in clause 2.5.3.3 on page 44, and clause 2.4.3.6 on page 21. This information is coded as the sampled value of a system clock.

The value of the system clock frequency is measured in Hz and shall meet the following constraints:

27 000 000 - 1 350 <= system_clock_frequency <= 27 000 000 + 1 350

rate of change of system_clock_frequency with time <= 75  10-3  Hz/s

The notation "system_clock_frequency" is used in several places in this proposed standard to refer to the frequency of a clock meeting these requirements.  For notational convenience, equations in which SCR, PTS, or DTS appear, lead to values of time which are accurate to some integral multiple of (300233/system_clock_frequency).  This is due to the encoding of SCR timing information as 33 bits of 1/300 of the system clock frequency plus 9 bits for the remainder, and encoding as 33 bits of the system clock frequency divided by 300 for PTS and DTS.

Input to the Program Stream system target decoder

Data from the ISO/IEC 13818 Program Stream enters the system target decoder.  The ith byte, M(i), enters at time tm(i).  The time at which this byte enters the system target decoder can be recovered from the input stream by decoding the input system clock reference (SCR) fields encoded in the pack header. The SCR, as defined in equation 2-17 , is coded in two parts; one, in units of 1/300  the system clock frequency, called SCR_base (equation 2-15 ), and one, called SCR_ext (equation 2-16 ), in units of the system clock frequency. The value encoded in the SCR(i') field indicates time tm(i'), where i' refers to the byte containing the last bit of the SCR_base field, M(i').

Specifically:

(2-15)
2-15

(2-16)
2-16

(2-17)
2-17

The input arrival time, tm(i), as given in equation 2-18, for all other bytes shall be constructed from SCR(i') and the rate at which data arrives, where the arrival rate within each pack is the value represented in the program_mux_rate field in that pack's header.

(2-18)
2-18

Where:

i'	is the index of the byte containing the last bit of the system_clock_reference base field in the pack header.

i	is the index of any byte in the pack, including the pack header.

SCR(i')	is the time encoded in the system_clock_reference base and extension fields in units of the system clock.

program_mux_rate	is a field defined in clause 2.5.3.3 on page 44.

After delivery of the last byte of a pack there may be a time interval during which no bytes are delivered to the input of the P-STD.

Buffering

The PES packet data from elementary stream n is passed to the input buffer for stream n, Bn.  Transfer of byte M(i) from the system target decoder input to Bn is instantaneous, so that byte M(i) enters the buffer for stream n, of size BSn, at time tm(i).

Bytes present in the pack header, system headers, or PES packet headers of the ISO/IEC 13818 Program Stream such as SCR, DTS, PTS, and packet_length fields, are not delivered to any of the buffers, but may be used to control the system.

The input buffer sizes BS1 through BSn are given by the P-STD buffer size parameter in the syntax in equation 2-13 and equation 2-14 on page 29.

At the decoding time, tdn(j), all the data for the access unit that has been in the input buffer longest (An(j)) is removed instantaneously.  In the case of an ISO/IEC 13818 video stream the decoding time, tdn(j), may be derived from subclauses C.9 to C.11 of annex C of ISO/IEC 13818-2.  The data defined as belonging to an ISO/IEC 13818 video access unit for this purpose is defined in subclause C.5  of annex C of ISO/IEC 13818-2.  In the case of an ISO/IEC 13818 audio stream access units consist of audio frames and are decoded at a time defined in ISO/IEC 13818-3.  As the access unit is removed from the buffer it is instantaneously decoded to a presentation unit.

When the low_delay flag in the video sequence extension is set to '1' (subclause 6.2.2.3 of ISO/IEC 13818-2) the VBV buffer may underflow.  In this case when the P-STD elementary stream buffer Bn is examined at the time specified by tdn(j), the complete data for the access unit may not be present in the buffer Bn.  When this case arises, the buffer shall be re-examined at intervals of two field-periods until the data for the complete acc

# Footnotes

ess unit is present in the buffer.  At this time the entire access unit and associated system data if any shall be removed from buffer Bn instantaneously.  Overflow of buffer Bn shall not occur.

VBV buffer underflow is allowed to occur continuously without limit.  The P-STD decoder shall remove access unit data from buffer Bn at the earliest time consistent with the p